WBS_2 Activity

21-FEB-02

• Legacy PBX-M Equipment Removal in Progress for NCSX

• Must be done before PBX-M removal starts May 02

• Legacy Inspections performed 2/13/02

• Legacy Tagging in progress

• Master Equipment List (MEL) transferals to NCSX

Subsystem Engineers in progress

• Removal of WBS_2 Site Credits started

• Timely and useful exercise at this time; impacting WBS_2 planning

• SOFE Jan 02, presented the Poster "Neutral Beam Injection Requirements And Design Issues  For The National Compact Stellarator Experiment"

• Seemed to be well received; no issues arose during presentation

• Discussion with D.Ciric, (Culham) re status of MAST NBI Long

NBI Upgrade (on track)

• Pumping Speed, Base Pressure

• Investigated W7-AS, LHD literature on vacuum performance

• Discussed W7-AS and LHD vacuum characteristics with encountered W7-AS and LHD physicists

• Conclusions: NSCX should have adequate pumping speed to achieve base pressures of ~2x 10E-8 torr and to pumpdown from expected prefill pressures sufficiently fast to accommodate ~ 5 min rep rate based on PBX-M service.

• Fringe Fields at Turbo Molecular Pumps (TMP)

• Fringe fields at PDX TMP estimated

• Art Brooks fringe field simulations (1102 case) used to estimate fringe fields at likely location of NCSX TMP's

• Conclusions: NCSX 1102 case fringe fields seem comparable to PDX 500 KA case but details depend on the final Cryostat and duct design

• Fringe Fields at NB Beamlines

• Art Brooks fringe field simulations (1102 case) used to estimate fringe fields at likely location of NB Beamlines

• NCSX 1102 fringe fields seem less than or comparable

to PDX 500 KA case

• Art Brooks given specific NB regions of interest to rerun

with finer resolution

• Final NBI position may be driven by major radius of the Cryostat which forces TMP and NBI TIV outwards

• NBI Duct Design

• Discussed with D.Johson installing angled ports on the NBI duct aimed at the Upper and Lower divertors, and possibly a midplane port

• Discussed this possibility and duct issues with M.Cole (ORNL)

• M. Cole forwarded useful drawings

• Modified an NCSX plan view layout to show a conceptual duct design that meets the requirements; reviewing with D. Johnson; will ship to M.Cole, T.Brown, and L.Morris

• Noted that the major radius of the Cryostat forces TMP and NBI TIV outwards.

• Reviewed WBS_2 Dictionary

• Good shape; minor clarification inserted into GDC description

• WBS_2 Cost Estimates

• Started with WBS_211, Gas Fuelling

- Inserted labor demographics into PVR Cost Estimates

- Transferred some Engineering work from Engineering

to a SuperTech

• Considering combining NBI WBS_251 (maintenance)

and _252 (realignment)

• Discussed NB Computerization with G.Oliaro,P. Sichta, P. Roney. G. Oliaro will  review WBS 25 NB computerization estimate

• Discussed with R.Majeski getting input for WBS_24, ICH; RF work still in progress

• All previously listed costs for moving and storage of PBX-M

site-credits will be removed

• CDR Conceptual Design Chapter

• Under Review for possible modifications

• May include updates on design progress on NB ducts, Torus Pumping, and other auxiliary systems

• The updated version will be used for consistent input into the CDR Engineering design description