VV Status	PLG 2/26

- New Vessel Model

-	Based on Art’s results.

- Improvements in progress, vessel still very “bumpy.”

-	Progress is slow (trial and error).

-	Likelihood of never being as smooth as original.

- Port stubs inside stayout zone removes some bulges.

- VV spec is being updated

- VV prototype update

- Need all comments and revisions.

- Do update in one final revision.

- Thermal analysis

-	Vessel cooling time independent of cooling medium.

- Can utilize water or gas (He or N2) at modest pressure.

- Consequence of low conductivity of Inconel (inverse Biot number, k/(h*L), very small) compared to heat transfer coef.

Issues	- Need definition:

# Magnetic loops

-	Outside of vacuum vessel?

- Loops

- Rogowski coils?

- Where will these be located?

### In-Vessel diagnostics

- Special tiles?