VACUUM VESSEL

BAKEOUT TRADEOFF           plg 10/27/03

Pros and cons of a vessel bakeable to 350 C.

COST/SCHEDULE

PROS	  CONS/AREAS OF CONCERN	COMMENTS	          INPACT

| 1. Eliminates need for PFC interior heating system. - less complexity - less cost | 1. 350 C only needed if Graphite is used during upgrade | 150 C is cheaper option for initial operation. . It is unknown at this stage whether or not graphite will ever be used. | 3 man-weeks. Redesign PFCs, revisit cost estimates. |
| --- | --- | --- | --- |
|  | 2. Tubing can not be grouted onto vessel with epoxy. - Welding tubes may entail large risks as distortion will occur. Installation would have to be done by PPPL unless vendor is given responsibility. - Welded tubes will require direct contact. - No attachment method for 350 service other than welding identified at present. | Exceeds epoxy max temp. R&D required to access risk. Requires renegotiation of contract if vendor responsible. Magnetic loops can not pass under. High temp adhesives under study. | TBD |
|  | 3. Heat load to coils will increase from 8.6 kW to 11.6 kW. | Study will be required to assure coil system will function adequately. | 3 man-weeks-Fan |
|  | 4. O-rings can not operate at 350 C. | Metal o-rings or, cooling of flanges to clamp them at lower temperature. New cooling loop required. | 4 man-weeks to add drawings, additional analysis. |
|  | 5. 350 C can not be attained using present He power system. Tracing pressure must be increased to20 atmos.. | He system upgrade to 29 kW @ 20 atmos. required. VV tracing system adequacy under study. | TBD |
|  | 6. High temperature effects on vessel. | Unknown effects at higher temperature; stress effects due to unlike matl and weld stresses must be intensified. Stress relief of entire vessel probably mandatory. | TBD |
|  | 7. Possible diagnostic issues | Need assurance from other WBS disciplines to assure there would not be problems with diagnostics and experiments. | TBD |
|  | 8. Effects on NB port uncertain. | Tradeoff study between welded and bolted transition duct is called for. Needs study where to transition material and how to clamp temperature. 3-D thermal modeling required. | TBD |
|  | 9. Vessel system must handle upgrade heat loads. | Need to study heat distribution and thermal gradient effects on vessel. | TBD |
|  | 10. Electric breaks | He piping ceramic breaks at 350 C need investigation. | TBD |
|  | 11. Geometrical growth of vessel outward | Need to check hot vessel for clearance | TBD |