TF notes:

TF not aligned with the modular coils at 80K but rather at RT.  A change in the requirements may be in order.  Calculate offsets and perhaps shim.

Is the 3-sided case on the outer leg identified as a procurement somewhere?  Ditto for the TF supports.

Is there a documented analysis of the clearances during assembly?  What clearances are provided for thermal insulation around the VV port extensions?