Questions

- Is alumina coating adequate electrically? (tracking distance, durability, etc)

- Are inboard bolts adequate for shear load?

- Will inboard bolts stay tight?

Hardware – buy now

- Buy enough spherical washers for one field period

- Buy enough bushing material for one field period (G11CR for now)

- Concern about supernut revolves around time to install – maybe ok, best from safety standpoint (no high pressure tensioners)

- Need to resolve length of studs

- Get enough supernuts for field period

- Get enough regular (12 point?) nuts for casting

- Shims

  - Water jet shape at PPPL

  - Machine thickness, angle at PPPL

  - Arrange BOA for 24 hour turn around at alumina coating company

Analysis

- Determine what the stud loads are with no friction between bolts

- Determine what the coil response is with the actual shim footprint/coverage

A-A fitup test (picked because we have them)

- Tom Brown calculates shim thickness for 3 shims

- Shims machined and A1 is set on A-2 using 3 shims to establish relative position

- Gap measured for other shims, compared with calculation

- Machine shims

- Apply Fuji film

Tests to try

- Inboard pincushion shim with plug welded pins

- Alumina coated steel bushing