Trial Shims

- Thickness range of shims with Alumina coating:  0.465-0.540”

- Profile:  Trial shims should be machined to the profile shown in the drawing below.

- Shims to be produced:  The thicknesses are to be per Table I.

Table I.  Trial shim thicknesses

| Shim Type # | Thickness of SS +/- 0.002 | Thickness with Alumina +/- 0.005 | No. Shims |  |
| --- | --- | --- | --- | --- |
| 1 | 0.455 | 0.465 | 4 |  |
| 2 | 0.455 | 0.470 | 4 |  |
| 3 | 0.455 | 0.475 | 4 |  |
| 4 | 0.455 | 0.480 | 6 |  |
| 5 | 0.470 | 0.485 | 6 |  |
| 6 | 0.470 | 0.490 | 6 |  |
| 7 | 0.470 | 0.495 | 8 |  |
| 8 | 0.485 | 0.500 | 8 |  |
| 9 | 0.485 | 0.505 | 8 |  |
| 10 | 0.485 | 0.510 | 8 |  |
| 11 | 0.495 | 0.515 | 6 |  |
| 12 | 0.495 | 0.520 | 6 |  |
| 13 | 0.515 | 0.525 | 6 |  |
| 14 | 0.515 | 0.530 | 4 |  |
| 15 | 0.515 | 0.535 | 4 |  |
| 16 | 0.515 | 0.540 | 4 |  |
|  |  | Total | 92 |  |

- Shim fit-up:

  - With the coils “gapped” to their proper position, each shim shall be hand fitted by choosing a shim thickness that is a snug fit.

  - Following this fit-up, the upper coil is to be slightly lifted with the crane and Fugi Paper shall be inserted above each shim.

  - The bolts shall be torqued to their full value using a bolt tightening sequence to be defined by MV and added herein.

- Fit-up evaluation:  The minimum permissible contact area, based on a bolt load value of 75,000 lbs. x 75%= 56250 lbs (to avoid over-stressing the Stellalloy threads in this trial) and a coefficient of friction of 0.7 is determined as follows:

Stellalloy properties

Shear allowable:  The allowable shear in the Stellalloy shall be taken to be 0.5 of the tensile allowable 0f 95 ksi with a safety factor of 0.8 – i.e., 0.5 x 95000 x 0.8= 38,000 psi.

The friction load imposed on a bolt with mu = 0.7 is 75000 x .7 = 56250 lbs.

Area Required:  Therefore the area required will be56250 lbs. /38,000 lbs/in^2 = 1.47 sq. in.

# Text boxes

At 77K					At RT

| Property | Required | C-1 Casting Heat 27728 (averages) | Required |  | C-1 Casting Heat 27728 (averages) |
| --- | --- | --- | --- | --- | --- |
| Elastic Modulus | 21 Msi (144.8 Gpa) | 23.3 Msi(1) | 20 Msi (137.9 Gpa) |  | 21.0 Msi(4) |
| 0.2% Yield Strength | 72 ksi (496.4 Mpa) | 98.4 Msi (1) 124 Msi(7) | 34 ksi (234.4 Mpa) |  | 34.2 ksi(4) |
| Tensile Strength | 95 ksi (655 Mpa) | 170.2 ksi(1) 170.2 ksi(7) | 78 ksi (537.8 Mpa) |  | 83.8ksi(4) |
| Elongation | 32% | 55% (1) 58.7% (7) | 36% |  | 51.5% (4) |
| Charpy V – notch Energy | 35 ft. lbs. (47.4 J) | 78 ft lbs.(2) | 60 ft-lbs (81.3 J) |  | 142 ft. lbs. (3) |