# Text boxes

attachment scheme:   weld 1” diameter  pins onto both flanges (say, 2/slider).  Insulate OD of pins with G10CR sleeves;  slide plates and G10CR would have clearance holes to permit them to simply be “hung” on the pins.

C-C Slide Concept

- Slide plates located top & bottom.

- Plates made of W7X material or possibly just G10CR.

- Base plate thicknesses on metrology measurements.

  - Initial assembly tolerance: aim for zero gap between sliders, but a gap of up to 0.010” is permissible to simplify assembly.

- An additional bolt & friction shim is added top and bottom to address bolt loading issue.

G10 CR CR pplates

Low friction slide plates

Slide assemblies

Flange B

SS bosses welded onto flanges to retain slider and G10 plates