### Revision 03/04/2000

### Inspection Log

| Job Number | 20021186 |
| --- | --- |

| Code | Name | Description |
| --- | --- | --- |
| OBSRV | Observation | Used when problems such as back-draft areas are noticed on customer supplied model. |
| NOTE | Note | General notes. |
| OK | OK |  |
| NCA | Needs Corrective Action | Used when item has a mistake and needs to be corrected. |
| NAW | Needs Additional Work | Used when item is not complete |
| MOD | Modification | Used when item is not necessarily wrong but needs modification in order to optimize |
| INV | Investigate | Used when something needs to be looked into or researched further. |

| Insp. No.: I05 | Insp: Jim W. | Date: 01/24/2003 Start: End: Hours: |
| --- | --- | --- |
| Reference Materials: | Print SE1405-003-1 (JC04a) |
| Inspection Objectives; Casting Measurements |

| A) | Casting-003-1_1 (SE1405-003-1) Casting #1 |
| --- | --- |
| 1) | Note | Spot-checked four sections on casting by comparing dimensions to those from SE1405-003-1 (JC04a). See casting-003-1_1.doc for results, and section-003-1.gif for areas checked. In dim #2 position #3a checked 1.875 could be put into tolerance if .750 dim. Is Reduced. |
| 2) | OBSRV | Casting ends are rounded should have been ground back to remove fillet Produced from machining sand mold @ Waukesha Foundry. See images end-003-1_1-1.jpg, end-003-1_1-2.jpg |
| 3) | Note | See image-003-1_1.jpg Entire picture of casting.(Quality of finish) |

| B) | Casting-003-1_2 (SE1405-003-1) Casting #2 |
| --- | --- |
| 1) | Note | Spot-checked four sections on casting by comparing dimensions to those from SE1405-003-1 (JC04a). See casting-003-1_2.doc for results, and section-003-1.gif for areas checked. In dim #2 all positions failed tolerance except for pos. 3b. Note These dim. Could be put in tolerance if .750 dim. Is reduced. |
| 2) | OBSRV | Casting ends are rounded should have been ground back to remove fillet Produced from machining sand mold @ Waukesha Foundry. See images end-003-1_2-1.jpg, end-003-1_2-2.jpg |
| 3) | Note | See image-003-1_2.jpg Entire picture of casting.(Quality of finish) |
| C) | Casting-003-2_1 (SE1405-003-1) Casting #1 |
| 1) | OK | Spot-checked four sections on casting by comparing dimensions to those from SE1405-003-1 (JC04a). See casting-003-2_1.doc for results, and section-003-2.gif for areas checked. All dimensions prove out per print SE1405-003-1 (JC04a) |
| 2) | OBSRV | Casting ends are rounded should have been ground back to remove fillet Produced from machining sand mold @ Waukesha Foundry. See images end-003-2_1-1.jpg, end-003-2_1-2.jpg |
| 3) | Note | See image-003-2_1.jpg Entire picture of casting.(Quality of finish) |

| D) | Casting-003-2_2 (SE1405-003-1) Casting #2 |
| --- | --- |
| 1) | OK | Spot-checked four sections on casting by comparing dimensions to those from SE1405-003-1 (JC04a). See casting-003-2_2.doc for results, and section-003-2.gif for areas checked. In dim #2 position #2a checked 1.918 could be put into tolerance if .750 dim. Is Reduced. |
| 2) | OBSRV | Casting ends are rounded should have been ground back to remove fillet Produced from machining sand mold @ Waukesha Foundry. See images end-003-2_2-1.jpg, end-003-2_2-2.jpg |
| 3) | Note | See image-003-2_2.jpg Entire picture of casting.(Quality of finish) |

General Notes;