### Revision 03/04/2000

### Inspection Log

| Job Number | 20021043 |
| --- | --- |

| Code | Name | Description |
| --- | --- | --- |
| OBSRV | Observation | Used when problems such as back-draft areas are noticed on customer supplied model. |
| NOTE | Note | General notes. |
| OK | OK |  |
| NCA | Needs Corrective Action | Used when item has a mistake and needs to be corrected. |
| NAW | Needs Additional Work | Used when item is not complete |
| MOD | Modification | Used when item is not necessarily wrong but needs modification in order to optimize |
| INV | Investigate | Used when something needs to be looked into or researched further. |

| Insp. No.: I04 | Insp: John P, Dean S | Date: 03/28/2003 Start: 10:30 am End: 12:30pm Hours: 2 hrs |
| --- | --- | --- |
| Reference Materials: | Machined Part |
| Inspection Objectives; Part Models modeled correctly |

| A) | Machined Part |
| --- | --- |
| 1) | OK | Dean Solberg from Exact Metrology came in with his Romer arm and inspected finished part. Results are documented in Inspection 04 excel sheet and jpg images. All data except holes are measured as deviation to cad model. All within tolerance. Hole data is XY position. Positions compared manually to cad model. All within tolerance. |