| JP Number: | 20031043 |
| --- | --- |
| Dimension Table: | 01 (I05) |

| No. | Insp. No(s) | Print Dim. | Calculated Dim. | Actual Variance | Model Level(s) | Notes | Code |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 04 | 48 ref | 48.00 (cad) | -.004 to + .002 |  | Measured points sp1 – sp39 under Profiles section show deviations of 4 profile surfaces. Since surfaces are within .006 so is overall. checked with Romer cmm. | OK |
| 2 | 04 | 19 ref | 19.015 (cad) | -.004 to .002 |  | Same as (1) | OK |
| 3 | 04 | 7 ref |  |  |  | Double dimensioned, See #13 | OK |
| 4 | 04 05 | .46 typ. | .463 (cad) 16 places | -.008 to .005 -.001 to .005 |  | Some points of Outer Pockets section were triggered on inside wall of these pockets. checked with Romer cmm. Checked with depth micrometer | OK |
| 5 | 04 | 1.50 typ | 16 places | -.008 to .005 |  | Some points of Outer Pockets section were triggered on side walls of these pockets. checked with Romer cmm. | OK |
| 6 | 04 05 | 3.00 typ | 16 places | -.008 to .005 -.000 to .006 |  | Some points of Outer Pockets section were triggered on side walls of these pockets. checked with Romer cmm. Checked with calipers | OK |
| 7 | 04 | 14.5 |  | -.004 to + .002 |  | Measured points sp1 – sp39 under Profiles section show deviations of 4 profile surfaces. Since surfaces are within .006 so is theoretical center. Holes 4, 6, 11 within specs. (.010 max) Hole 13 show .020 out due to probe measuring chamfer. Chamfer is slightly off center (visible). checked with Romer cmm. | OK OK |
| 8 | 04 | 28.985 |  | -.004 to + .002 |  | Measured points sp1 – sp39 under Profiles section show deviations of 4 profile surfaces. Since surfaces are within .006 so is theoretical center. Holes 2, 7, 9, 15 within specs. (.010 max) checked with Romer cmm. | OK |
| 09 | 04 | 45deg typ | 4 places | -.004 to + .002 |  | Measured points sp1 – sp39 under Profiles section show deviations of 4 profile surfaces. Since surfaces are within .006 so is theoretical angle. Holes 17,,20,21,24 within specs. (.010 max) checked with Romer cmm. | OK |
| 10 | 04 | .46 typ. |  |  |  | Double dimensioned, see #4 | OK |
| 11 | 04 | 7 | 2 places | -.006 to +.003 |  | Holes 18,23 checked with Romer cmm. | OK |
| 12 | 04 | 7 | 2 places | -.010 to +.002 |  | Holes 19,22 checked with Romer cmm. | OK |
| 13 | 04 | 7.188 to CL |  | -.004 to + .002 |  | Measured points sp1 – sp39 under Profiles section show deviations of 4 profile surfaces. Since surfaces are within .006 so is theoretical center. checked with Romer cmm. | OK |
| 14 | 04 | 1.95typ | 1.945(cad) | -.004 to + .002 -.005 to .000 |  | Measured points sp1 – sp39 under Profiles section show deviations of 4 profile surfaces. Since surfaces are within .006 so is theoretical demension. checked with Romer cmm. checked with depth micrometer | OK |
| 15 | 04 | .750 | .750(cad) | -.004 to + .002 .750 thickness within -.001 to .001 |  | Measured points sp1 – sp39 under Profiles section show deviations of 4 profile surfaces. Since surfaces are within .006 so is theoretical dimension. checked with Romer cmm. checked with micrometer | OK |
| 16 | 04 | .375 | .375(cad) | -.004 to + .002 .750 thickness within -.001 to .001 |  | Measured points sp1 – sp39 under Profiles section show deviations of 4 profile surfaces. Since surfaces are within .006 so is theoretical dimension. checked with Romer cmm. checked with micrometer | OK |
| 17 | 04 | 5.200 | 5.200(cad) | -.002 to .001 |  | checked with depth micrometer | OK |
| 18 | 04 | 1.500 | 1.500(cad) | -.003 to .002 |  | checked with micrometer | OK |
| 19 | 04 | 1.200 | 1.200 (cad) |  |  | Measured Holes C1-C16 all within specs. (.010max) checked with Romer cmm. | OK |
| 20 | 04 | ½ pipe taps |  |  |  | depth measured with pipe tap gage | OK |
| 21 | 04 | 1.200 | 1.200 (cad) |  |  | Measured Holes C1-C16 all within specs. (.010max) checked with Romer cmm. | OK |
| 22 | 04 | 2.320 | 2.320 (cad) | -.004 to + .002 |  | Measured points sp1 – sp39 under Profiles section show deviations of 4 profile surfaces. Since surfaces are within .006 so is theoretical demension. checked with Romer cmm. | OK |
| 23 | 04 | 4.640 | 4.640 (cad) | -.004 to + .002 |  | Measured points sp1 – sp39 under Profiles section show deviations of 4 profile surfaces. Since surfaces are within .006 so is theoretical demension. checked with Romer cmm. | OK` |
| 24 | 04 | 3/8-16x.750 |  |  |  | depth and thread measured with tap gage | OK |
| 25 | 04 | .46 typ. |  |  |  | Double dimensioned, see #4 | OK |
| 26 | 04 | R.13 typ. | .125 (cad) |  |  | Checked with Starrett radius gage | OK |
| 27 | 04 | 1.000 typ. | 1.000 (cad) | -.001 to .001 |  | checked with depth micrometer | OK |
| 28 | 04 | 4.64 |  |  |  | Double dimensioned, see 23 | OK |

General Notes: