# Text boxes

Casting

- Half-lapped layer of composite:

  - 0.007 in. thick glass [2 inch nom. wide] & 0.0065(HN) Kapton [1.5 nom. wide] with adhesive

  - X 2 = 0.027 in. thick

(1) Butt lapped layer of composite:

-0.007 in. thick glass [2 inch nom. wide] and 0.0035 (HN) Kapton [1.5 nom. wide]) with adhesive

(1) Butt lapped layer

0.007 in. thick S-2 glass [2 inch nom. wide]

0.027 in.

0.007 in.

0.0105 in.

1

1

2

2

3

3

0.0445 in. overall

May 4, 2004

J.H. Chrzanowski

0.25 in.

1.5 in.

Tracking distance = 1.0 inches