# ENGINEERING REPLY FROM:   Mike Boivin                  DATE: August 2, 2001

SUBJECT: Compacted Copper Cable

CUSTOMER: ORNL

SALESPERSON: Carl

REQUEST:

Rectangular Compacted Copper Cable

12,240 strands of 36 awg

300MCM 12x5/3/68/36 Bare Copper with Single Nylon Serve to 0.500” x 0.625”

BUNCH 68/36 BARE COPPER AT 1-1/2” RHL TO 0.048” ± 0.002” OD

Bunch (medium)

BUNCH 3/68/36 BARE COPPER AT 3” RHL TO 0.082” ± 0.003” OD

Bunch (Heavy)

BUNCH 5/3/68/36 BARE COPPER AT 3” RHL TO 0.184” ± 0.006” OD

Nextrom

CABLE 12X5/3/68/36 BARE COPPER

CABLE 9 @ 3 AT 6” LHL TO 0.710” ± 0.015” OD

NOTE: USE DIE EQUAL TO NOM OD (973.5#/M’)

SINGLE NYLON SERVE – USE 20-END 70 LT NYLON, 50% LAP RHL TO 0.715” OD ± 0.015” (8.15#/M’)

SQUARE USING 4U TURKSHEAD TO 0.500” ± 0.010” BY 0.625” ± 0.010”