CTD-528 "Super Tuff"

for Cryogenic Applications

High Performance for Vacuum Impregnation and Wet-Winding Applications

Long Pot Life and Near Room Temperature Cure in Less than 24 hours

¥	A special "super tuff" formulation, with a primary amine cure, very low viscosity, low vapor pressure, and a high amine content.

¥	Ideally suited for applications where extended pot life and low to moderate exothermic heat of reaction is needed.

¥	Low viscosity, long pot-life, and near ambient temperature cure yields quick component processing.

¥	Non-carcinogenic resin system with very low toxicity.  It is a non-solvent based system, and will not give off volatiles on cure.

¥	Wide range of properties and applications: can be used as a neat resin for fiber reinforcement, or with particulate fillers - physical properties (thermal expansion, thermal and electrical conductivities) can be tailored to meet differing requirements.

Cure: 		         	   2 Hrs. @ 80¡C;

7 Days @ 25¡C (>90% of properties will be obtained in 72 hours)

OPTIONAL POST CURE: 4 Hrs @ 125¡C

Gel Time:				Approximately 3 to 4 Hours in 3 Gallon Quantity

(Consult CTD for additional information)

Mix Proportions :				Part A			Part B

(Parts By Weight)           (Parts By Weight)

CTD-528				             100 		                  60

Fillers can be added as needed

Mixing Temperature:		20 - 30 ¡C (Room Temperature)

Process Compatabilities

Resin Transfer Molding (RTM)

Resin Injection Molding (RIM)

Filament winding (FW)

Vacuum Pressure Impregnation (VPI)

Casting with or without filler

Wet-winding

Advantages

* Non-Carcinogenic

* Low Toxicity

* Long Pot-Life

* Very Low Viscosity, <1000 cps @ 25¡C

* Excellent adhesion to fibers and fillers

* Specific Gravity  < 1.2 g/cc

CTD-528 Processing Characteristics

Viscosity Over Time

CTD-528 Properties

Compression:                                  Temperature  [K]		Strength [Ksi]

54% vf E Glass		                   76     		    134.3

Short Beam Shear                           Temperature  [K]                 Strength [Ksi]

54% vf E Glass		       	       76			      20.8

Disclaimer:  The information and recommendations contained herein are based upon data believed to be accurate. However, no guarantee or warranty of any kind expressed or implied is made with respect to the information contained herein.

Feb 98

CTD-528-CG20

Viscosity Vs. Time Data

Comparing 20¡C with 30¡C for 10 gram quantity

Large Quantity (approximately 3 gallons) was tested for gel time at 20¡C.  After about 3.5 hours, temperature of the resin exceeded about 38.5¡C.  At this point the temperature increase accelerated and gel occurred shortly thereafter.

Extrapolating the data above for the gel time for 3 gallons of material at 30¡C, estimated gel time should be around 1.5 to 2.0 hours.  It is recommended to monitor the temperature of the bulk material.  When it exceeds 36 to 38¡C, that batch of material should be discarded.

Furthermore, it is recommended to mix up smaller quantities and then add additional material as the supply is depleted.  Customers have reported using this method for filament winding processes and have been able to utilize a resin batch for an entire day without having to clean it or have the material gel in the bath.

Once the material is in a smaller mass or has a higher surface area, such as in the transfer line, the gel time should increase beyond recommendations made above.  It is suggested that the temperature of the material in the tubes also be monitored.

May 99