# Text boxes

# Station No.1

Casting Preparation

102 Working Days per coil

Casting Preparation station.  Activities include:

-Mount casting to support ring

-Measure/inspect casting surfaces

-Install clamp studs

-Clean & mold release casting

-Install winding clamps

-Install inner cladding

Manpower:  2 technicians per station

DURATION: 15 working days per coil

# Station No.3

Winding/Molding Station B

# Station No.2

Winding/Molding Station A

Three winding stations will be used.  Each station will include:

-Coil winding

-Ground wrapping

-Installation of chill plates

-Installation bag mold

-Vacuum leak checking of bag

Manpower:  2 technicians per station

DURATION: 63 working days per coil

-38 days winding

-25 days chill plates and bag mold

# Station No.4

Winding/Molding Station C

J.H.Chrzanowski

8/20/04

# Station No.5

VPI/Autoclave Station

Install MC into autoclave; VPI and cleanup

Manpower:  4 technicians per station

DURATION: 12 working days per coil

# Station No.1

Casting Preparation

# Station No.6

Coil Testing

Transport VPI’d coil back to Station #1 Turning fixture for installation of Final Coil Clamps

Manpower:  2 technicians per station

DURATION: 5 working days per coil

Cold test the modular coil [TC Basement]

Manpower:  see Ron S. breakout

DURATION: 7 working days per coil

Note:  Once there are a sufficient number of castings delivered, a MC will leave the winding/molding stations every 21 days

Assumes a MCWF is delivered every 20 working days