# Text boxes

# Station No.1

Casting Preparation

Winding Form Preparation station:.  Activities include:

-Mount WF to support ring

-Measure/inspect WF surfaces

-Install clamp studs

-Clean & mold release WF

-Install winding clamps

-Install inner cladding

Manpower:  2 technicians per station

# Station No.3

Winding/Molding Station B

# Station No.2

Winding/Molding Station A

Three winding stations will be used.  Each station will include:

-Coil winding

-Ground wrapping

-Installation of chill plates

-Installation bag mold

-Vacuum leak checking of bag

Manpower:  2 technicians per station

# Station No.4

Winding/Molding Station C

# Station No.5

VPI/Autoclave Station

Install MC into autoclave; VPI and cleanup

Manpower:  4 technicians per station

# Station No.1

Post VPI

# Station No.6

Coil Testing

Transport VPI’d coil back to Station #1 Turning fixture for installation of Final Coil Clamps

Manpower:  2 technicians per station

Cold test the modular coil [TC Basement]