# Text boxes

# Station No.6

Coil Testing

Basement Activities

- Coil Testing Activities

  - Cold test the modular coil

  - Store tested MC

Material Receipt

- Material Receipt

  - Conductor receipt & inspection

  - Casting receipt & inspection

  - General product inspection guidelines

# Station No.3

Winding Station B

# Station No.2

Winding Station A

- Winding Operations

  - Install inner ground wrap insulation

  - Position leads for side “A” winding

  - Wind side “A” of modular coil

  - Complete leads for side “A” winding

  - Coil Measurements/electrical tests

  - Rotate coil

  - Position leads for side “B” winding

  - Wind side “B” of coil

  - Positioning leads for side “B” winding

  - Complete ground wrap sides A & B

# Station No.4

Molding/VPI Preparation

- Molding & VPI Preparation

  - Install outer Diagnostics

  - Install Outer Chill plates

  - Install bag mold

  - Vacuum leak check bag

  - Install final coil clamps

# Station No.5

VPI/Autoclave Station

- VPI/Autoclave Activities

  - Install coil in autoclave and prepare coil for VPI

  - Vacuum impregnate coil

  - Cleanup and install final coil clamps

  - Transport coil to Test Facility

# Station No.1

Casting Preparation

Winding Facility Activities

- Casting Preparation

  - Mount casting to support ring

  - Measure casting surfaces

  - Install clamp studs

  - Clean & mold release casting

  - Install inner chill plates

  - Install Diagnostics