JOB HAZARD ANALYSIS

Reference:

Work Order #     	 Work Permit #     Work Planning #1138   Procedure #D-NCSX-MCF-004-02    Other

| Written by (Print):Jim Chrzanowski Date: 9/18/06 Division/Branch/Org: NCSX Writer must inform affected workers of hazards and controls on the JHA, prior to commencement of work. [ X Pre-Job Brief ] |
| --- |
| Description & Location (Room/Building) of job/work to be performed: Modular Coil Stations 1a & 1b Activities include: Removal of epoxy shell/bag mold and winding clamp studs, brazing, electrical & pneumatic testing, installation of clamps, strain gauges, thermocouples and termination of cooling tubes. |
| Hazard (Check-off and Describe the source of the hazard) | Control Measures (See reference to safety notes in procedure D-NCSX-MCF-004-02 | See Back |
| X Chemicals a Acetone and ethanol for cleaning, expandable urethane | X MSDS's Available Training Provided [eye protection, Nitrile gloves] See relevant safety notes in procedure |  |
| Ergonomic Issues (Repetitive Motion, Lifting, Physical Stresses, etc.) b | Contact IH for briefing |  |
| Ionizing Radiation [Health Physics-HP] | Radiation Work Permit (RWP) |  |
| Non-Ionizing Radiation (Lasers, Magnetic Fields (EMF), RF, etc.) | Contact IH for high power lasers/EMF/RF Laser Safety Training |  |
| Environmental Impacts (Causing Environmental Release, Creating Hazardous Wastes, etc.) [M&ES] | Contact M&ES for guidance |  |
| X Noise c During use of impact wrenches | X Hearing Protection [ear plugs optional] |  |
| XSharp objects/tools d During removal of epoxy/glass shell mold | [Wear Kevlar or leather gloves] See relevant safety notes in procedure |  |
| Working Surfaces / Tripping Hazards e |  |  |
| Falls / Elevated Work f | Fall Protection Training |  |
| X Ladders / scaffolds / man-lifts During transfer of coil from station 1b to station 1a | X Inspection Training See relevant safety notes in procedure |  |
| X Cranes / rigging / Forklifts Lifting winding forms | X Trained/Qualified Personnel Hard hats required |  |
| XWelding / cutting / grinding / open flame Grinding of studs, Brazing & stud welding activities | X Hot Work Permit [ESU] [Safety glasses, FR clothing, welders or leather gloves] See relevant safety notes in procedure |  |
| X Impairing a Security / Fire System [ESU] During welding, brazing and grinding activities | X Contact Security Obtain flame permit |  |
| X Hot Surfaces / Cryogenics Parts brazed or stud welded | Cryogenic Training [Leather gloves] |  |
| Heat or Cold Stress g |  |  |
| Steam |  |  |
| X Electrical h [Electrical Safety] Final electrical testing of the modular coil | Lockout/Tagout Arc Flash Analysis h GFCI Trained Personnel See relevant safety notes in procedure |  |
| Confined Space / Oxygen Deficiency | Confined Space Permit |  |
| X Machinery / Machine tools Turning fixtures | X Machine Guards Chip Guards |  |
| X Hand Tools / Power Tools I Use of pneumatic impact wrenches | GFCI [Safety glasses] See relevant safety notes in procedure |  |
| X Eye Hazards j During brazing/welding/grinding, use of impact wrenches, chemical use, pneumatic testing | [Safety glasses, welders glasses, chemical goggles, face shield] See relevant safety notes in procedure |  |
| X Falling Objects During crane operation | Wear hard hats whenever crane is in overhead use |  |
| Potential / Stored Energy k |  |  |
| X Foot Hazard Casting to ring plates are heavy (30 – 50 #) | X Safety Shoes [During the disassembly of coil to support ring] See relevant safety notes in procedure |  |
| Trenching / Digging | Digging Permit |  |
| Wall / Floor Penetrations | Penetration Permit |  |
| For questions about these topics, contact Industrial Hygiene (IH) except where noted in [brackets]. IH = 2533, 2531, %546, 639. HP = 2311, 2315. M&ES = 3380. ESU/Security = 2536, Electrical Safety = 3740 |

|  Access / Escape / Communications Concerns l |  |  |
| --- | --- | --- |
| Biological (Bodily fluids, Insects, Poison plants) |  |  |
| Vehicle Use / Fuel / Exhaust m |  |  |
| Illumination (inadequate lighting) |  |  |
| Working Alone n | IH Must Review/Approve Contact Security |  |
| Pressure / Vacuum (cylinders, pressure tests) | Compressed Gas Training |  |
| Others: |  |  |
| Comments: |

| Control Measures (Write the number of the appropriate control next to the hazard to which it applies) |
| --- |
| Engineering Controls | Administrative Controls | Personal Protective Equipment (PPE) |
| 01 - Platforms, Scaffolds | 12 - Procedures | 23 - Hard Hats | 29 Safety Glasses/Goggles |
| 02 - Use less hazardous chemicals | 13 - Specific training for job/location | 24 - Face Shields | 30 - Coveralls |
| 03 - Machine Guards, Chip Guards | 14 - Worker Rotation, Rest Breaks | 25 - Safety Shoes | 31 - Boots / Booties |
| 04 - Ventilation (fume hoods, elephant trunks, local exhaust systems) | 15 - Permits (Confined Space, RWP, Hot Work, Digging, Penetrations, Flame) | 26 - Ear Plugs/ Muffs | 32 - Gloves (leather, kevlar, neoprene, nitrile, voltage rated) |
| 05 - Fall Protection (Guardrails, toe boards) | 16 - Signs & Labels, Warning alarms (“high level”) | 27 - Respirator / Dust Mask | 33 - Full Body Harness & lanyards |
| 06 - Engineered Equipment Design | 17 - System or Job Walk down | 28 - Lab Coat / Apron | 34 - Flame retardant / flash resistant clothing |
|  |  | 35 – Electrically insulated Mat / Tools |
| 07 - Noise enclosure, absorption, mufflers | 18 - Safety watch, Buddy System | Emergency Equipment: |
| 08 - Vibration dampeners | 19 - Lockout/Tagout | 36 - Fire Extinguishers | 40 - Retrieval Gear. |
| 09 - Temporary lights | 20 - Spill Containment | 37 - Telephones/Radios | 41 - First Aid Equip, |
| 10 - Welding Screens | 21 - Barricades | 38 - Sprinkler System | 42 - Alarms |
| 11 - Mechanical lifting aids | 22 - Training / Qualification / Certification | 39 - Eye Washes & Safety Showers |
| *Explanations & Notes: |
| a Chemicals: List names or types of chemicals to be used. Be sure to use proper protective equipment for the chemical (one glove material will not protect against all chemicals). Contact Industrial Hygiene for more information and proper PPE selection. |
| b Ergonomics: Never lift more than 50 pounds. Frequent lifting of lighter weight objects can also cause injury. Repeating body motions frequently (such as continual use of wrenches) can cause injury. Industrial Hygiene should be consulted prior to activity to aid in preventing injuries. |
| c Noise: High noise can damage hearing. If you must shout to be understood 3 feet away, you may be damaging your hearing. Both noisy areas and loud tools must be considered. |
| d Sharp Objects/Tools: Sheet metal, knives, razor blades, metal which has been cut or machined, may cause cuts or punctures. Cut resistant gloves (such as Kevlar) must be worn. Leather is NOT a cut resistant material. |
| e Working Surfaces: Consider slip/trip/fall hazards, tight areas, uneven floors, holes. |
| f Falls: Personnel working on surfaces with edges 6 feet or more above another surface must be protected by guardrails or personal fall arrest systems. |
| g Heat/Cold Stress: Take frequent breaks, dress properly. |
| h Electrical: Use Lockout/Tagout procedures (see procedure ESH-016). No working live over 50 volts. For high voltage work contact AC Power. Arc Flash Analysis done per NFPA 70E. Section 130 |
| i Power tools: Must use proper extension cords and GFCI. |
| j Eye hazards: Splashes, dust, flying particles, bright light, UV. Eye washes, when required, are to be within 100 ft., or 10 seconds walking time. |
| k Potential / Stored Energy: Examples include: Compressed springs (could release), unbalanced objects (could fall), capacitors (stored electricity), fan blades (could free rotate), hydraulics (under pressure). Secure, lock and tag as appropriate. |
| l Access/Escape concerns: Preplan rescue and emergency egress. |
| m Vehicle use: Be aware of all vehicle concerns including being struck by vehicles (auto, construction vehicles, etc.), carbon monoxide exposure from exhausts, fire or leaks of fuel, etc. Back-up alarms on vehicles must be working. Training required for Forklifts. |
| n Working alone: Any hazardous work that will be performed alone must be reviewed & approved by IH on the JHA |
| Industrial Hygiene Review Required? Yes No ¦ IH Signature: Date |
| Other Review Required? Yes No ¦ Who? Signature: Date |
| Responsible Line Manager (RLM) Approval (as required by Division/Project) ¦ Signature: Date: |
| Personnel Briefed on this JHA: |

SEND Original to: Industrial Hygiene (Required)