JOB HAZARD ANALYSIS

Reference:

Work Order #     	 Work Permit #     	 Work Planning #1138	 Procedure #D-NCSX-RP-STEL-058 Other

| Written by (Print): James H. Chrzanowski Date:8/1/06 Division/Branch/Org:NCSX Writer must inform affected workers of hazards and controls on the JHA, prior to commencement of work. [x Pre-Job Brief ] |
| --- |
| Description & Location (Room/Building) of job/work to be performed: Make repairs to the C1 lead area. Work will be performed in the NCSX Winding facility [TFTR test cell] |
| Hazard (Check-off and Describe the source of the hazard) | Control Measures (Write # of Control(s) in Box) | See Back |
| x Chemicals a CTD-540 (2) Part epoxy system [small qualities will be used by brushing or using a syringe] | XMSDS's Available Training Provided Chemical goggles and Nitrile gloves |  |
| Ergonomic Issues (Repetitive Motion, Lifting, Physical Stresses, etc.) b | Contact IH for briefing |  |
| Ionizing Radiation [Health Physics-HP] | Radiation Work Permit (RWP) |  |
| Non-Ionizing Radiation (Lasers, Magnetic Fields (EMF), RF, etc.) | Contact IH for high power lasers/EMF/RF Laser Safety Training |  |
| Environmental Impacts (Causing Environmental Release, Creating Hazardous Wastes, etc.) [M&ES] | Contact M&ES for guidance |  |
| Noise c | Hearing Protection |  |
| x Sharp objects/tools d Knives and chisels may be used | Wear leather gloves if possible- extreme care |  |
| Working Surfaces / Tripping Hazards e |  |  |
| Falls / Elevated Work f | Fall Protection Training |  |
| Ladders / scaffolds / manlifts | Inspection Training |  |
| Cranes / rigging / Forklifts | Trained/Qualified Personnel |  |
| Welding / cutting / grinding / open flame | Hot Work Permit [ESU] |  |
| Impairing a Security / Fire System [ESU] | Contact Security |  |
| Hot Surfaces / Cryogenics | Cryogenic Training |  |
| Heat or Cold Stress g |  |  |
| Steam |  |  |
| x Electrical h [Electrical Safety] Megger tests will be performed | Lockout/Tagout Arc Flash Analysis h GFCI x Trained Personnel Electrical safety mat, ground stick and flashing lights are required |  |
| Confined Space / Oxygen Deficiency | Confined Space Permit |  |
| Machinery / Machine tools | Machine Guards Chip Guards |  |
| Hand Tools / Power Tools I | GFCI |  |
| x Eye Hazards j Working with epoxy | Chemical goggles required |  |
| Falling Objects |  |  |
| Potential / Stored Energy k |  |  |
| Foot Hazard | Safety Shoes |  |
| Trenching / Digging | Digging Permit |  |
| Wall / Floor Penetrations | Penetration Permit |  |
| For questions about these topics, contact Industrial Hygiene (IH) except where noted in [brackets]. IH = 2533, 2531, %546, 639. HP = 2311, 2315. M&ES = 3380. ESU/Security = 2536, Electrical Safety = 3740 |

|  Access / Escape / Communications Concerns l |  |  |
| --- | --- | --- |
| Biological (Bodily fluids, Insects, Poison plants) |  |  |
| Vehicle Use / Fuel / Exhaust m |  |  |
| Illumination (inadequate lighting) |  |  |
| Working Alone n | IH Must Review/Approve Contact Security |  |
| Pressure / Vacuum (cylinders, pressure tests) | Compressed Gas Training |  |
| Others: |  |  |
| Comments: |

| Control Measures (Write the number of the appropriate control next to the hazard to which it applies) |
| --- |
| Engineering Controls | Administrative Controls | Personal Protective Equipment (PPE) |
| 01 - Platforms, Scaffolds | 12 - Procedures | 23 - Hard Hats | 29 Safety Glasses/Goggles |
| 02 - Use less hazardous chemicals | 13 - Specific training for job/location | 24 - Face Shields | 30 - Coveralls |
| 03 - Machine Guards, Chip Guards | 14 - Worker Rotation, Rest Breaks | 25 - Safety Shoes | 31 - Boots / Booties |
| 04 - Ventilation (fume hoods, elephant trunks, local exhaust systems) | 15 - Permits (Confined Space, RWP, Hot Work, Digging, Penetrations, Flame) | 26 - Ear Plugs/ Muffs | 32 - Gloves (leather, kevlar, neoprene, nitrile, voltage rated) |
| 05 - Fall Protection (Guardrails, toe boards) | 16 - Signs & Labels, Warning alarms (“high level”) | 27 - Respirator / Dust Mask | 33 - Full Body Harness & lanyards |
| 06 - Engineered Equipment Design | 17 - System or Job Walk down | 28 - Lab Coat / Apron | 34 - Flame retardant / flash resistant clothing |
|  |  | 35 – Electrically insulated Mat / Tools |
| 07 - Noise enclosure, absorption, mufflers | 18 - Safety watch, Buddy System | Emergency Equipment: |
| 08 - Vibration dampeners | 19 - Lockout/Tagout | 36 - Fire Extinguishers | 40 - Retrieval Gear. |
| 09 - Temporary lights | 20 - Spill Containment | 37 - Telephones/Radios | 41 - First Aid Equip, |
| 10 - Welding Screens | 21 - Barricades | 38 - Sprinkler System | 42 - Alarms |
| 11 - Mechanical lifting aids | 22 - Training / Qualification / Certification | 39 - Eye Washes & Safety Showers |
| *Explanations & Notes: |
| a Chemicals: List names or types of chemicals to be used. Be sure to use proper protective equipment for the chemical (one glove material will not protect against all chemicals). Contact Industrial Hygiene for more information and proper PPE selection. |
| b Ergonomics: Never lift more than 50 pounds. Frequent lifting of lighter weight objects can also cause injury. Repeating body motions frequently (such as continual use of wrenches) can cause injury. Industrial Hygiene should be consulted prior to activity to aid in preventing injuries. |
| c Noise: High noise can damage hearing. If you must shout to be understood 3 feet away, you may be damaging your hearing. Both noisy areas and loud tools must be considered. |
| d Sharp Objects/Tools: Sheet metal, knives, razor blades, metal which has been cut or machined, may cause cuts or punctures. Cut resistant gloves (such as Kevlar) must be worn. Leather is NOT a cut resistant material. |
| e Working Surfaces: Consider slip/trip/fall hazards, tight areas, uneven floors, holes. |
| f Falls: Personnel working on surfaces with edges 6 feet or more above another surface must be protected by guardrails or personal fall arrest systems. |
| g Heat/Cold Stress: Take frequent breaks, dress properly. |
| h Electrical: Use Lockout/Tagout procedures (see procedure ESH-016). No working live over 50 volts. For high voltage work contact AC Power. Arc Flash Analysis done per NFPA 70E. Section 130 |
| i Power tools: Must use proper extension cords and GFCI. |
| j Eye hazards: Splashes, dust, flying particles, bright light, UV. Eye washes, when required, are to be within 100 ft., or 10 seconds walking time. |
| k Potential / Stored Energy: Examples include: Compressed springs (could release), unbalanced objects (could fall), capacitors (stored electricity), fan blades (could free rotate), hydraulics (under pressure). Secure, lock and tag as appropriate. |
| l Access/Escape concerns: Preplan rescue and emergency egress. |
| m Vehicle use: Be aware of all vehicle concerns including being struck by vehicles (auto, construction vehicles, etc.), carbon monoxide exposure from exhausts, fire or leaks of fuel, etc. Back-up alarms on vehicles must be working. Training required for Forklifts. |
| n Working alone: Any hazardous work that will be performed alone must be reviewed & approved by IH on the JHA |
| Industrial Hygiene Review Required? Yes No ¦ IH Signature: Date |
| Other Review Required? Yes No ¦ Who? Signature: Date |
| Responsible Line Manager (RLM) Approval (as required by Division/Project) ¦ Signature: Date: |
| Personnel Briefed on this JHA: |

SEND Original to: Industrial Hygiene  (Required)