## Termination of cooling tubes:

Each of the cooling tubes must be terminated to accommodate the final connection to the modular coil cooling system.

### Using approved NCSX drawings carefully cut each of the cooling tubes to correct length using a tube cutter.

### Once the tubes have been cut carefully form the cooling tubes as shown in Figure 4- Termination of Cooling Lines.

### Apply heat shrink Teflon tubing over the cooling tubes from the point where the tubes exit the chill plates through the clearance holes in the winding forms. [Figure 3 - Cooling Tube Sleeving Insulation]  Do not shrink the sleeving at this time.  Pull the sleeving away from the clearance holes until the couplings have been brazed in place.

Figure 3 - Cooling Tube Sleeving Insulation

Figure 4- Termination of Cooling Lines

# Text boxes

Heat-shrink sleeving [typ] from chill plates through winding form

Outside of winding form