Testing of the C1 Coil

July 17, 2006

NCSX-TEST-14-001-00-dA

DRAFT

Prepared by: ___________________________________________________________________________

Wayne Reiersen

Reviewed by: __________________________________________________________________________

Geoff Gettelfinger

Reviewed by: __________________________________________________________________________

Kevin Freudenberg

Reviewed by: __________________________________________________________________________

David Williamson

Reviewed by: __________________________________________________________________________

Art Brooks

Approved by: __________________________________________________________________________

Brad Nelson

# Executive Summary

# Test Setup

## Instrumentation

### Thermocouples

Eighteen Type E thermocouples were installed in the test setup.  The data acquisition system provided six channels for thermocouple data.  The locations for the thermocouples are listed in Table 5-1.  Two thermocouples (TC2 and TC3) were embedded in deep holes in the winding form.  One thermocouple was installed on the exterior of the winding pack (TC17).  One thermocouple was installed on an inboard supply coolant tube (TC7) and another on an outboard return coolant tube (TC9).  Thermocouples were typically insulated with bat insulation from the cryostat environment to avoid convective cooling of the thermocouple directly.  The final channel monitored the temperature inside the cryostat near the midplane elevation (TC18).

### Strain gages

Fifteen strain gages were installed.  The strain gages were manufactured by Vishay (H06A-AC1-125-700).  The data acquisition system provided fourteen operable channels for the strain gage data.  The locations for the strain gages are listed in Table 5-2.  Of the fourteen operable channels, ten channels monitored strain gages mounted on the winding form.  Nine of these strain gages were mounted at the base of the tee.  The tenth was mounted on the exterior surface of the winding form near where the leads penetrate the winding form.  The active strain gages mounted on the winding form were paired with dummy strain gages mounted approximately 1 inch off the winding form on a stainless steel substrate connected to the casting with a stud.  Strain gages were typically insulated with bat insulation to avoid introducing temperature differences between the active and dummy gages due to convective cooling.  Some strain gages, e.g., SG15, had a copper sleeve around the stud for improved thermal contact.  The intent of the dummy gages was to remove the thermal output so the apparent strain reflected the true mechanical strain.  Photographs of strain gage installations (without thermal insulation) are provided in Figure 6-11 through Figure 6-16.

The remaining four strain gages were installed on the exterior of the winding pack.  There was no substrate to mount dummy gages so the dummy gage was actually installed on the winding pack on the opposite side of the tee.  This was intended to remove the thermal output from cooldown to cryogenic temperature.  However, the apparent strain due to EM loading during a pulse would be the difference between these two active gages.  Strain gages mounted on the winding pack are apparent in Figure 6-11.

The strain gages mounted at the base of the tee and on the winding pack were oriented either in the direction of the winding pack or normal (transverse) to the direction of the winding pack.  Typically, two strain gages, one in the direction of the winding pack and one in the transverse direction were installed at each of the clamp locations selected as shown in Figure 6-13.

### Deflection monitor

# Test Results

## Cooldown

Cooldown of the C1 coil began on June 11 and continued until shots began to be taken on June 15.  Cooldown was initiated by introducing product from the LN2 supply line.  The line is used intermittently so initially, the product was warm gas.  A maximum temperature difference of 50K was administratively enforced during cooldown.  As the line cooled, so did the gas being supplied until eventually it became 2-phase product and then liquid.  The liquid was caught in a tank in the center of the cryostat.  The tank measured 12” on each side.  The liquid column was approximately 28” tall.

During the first 40 hours, the cooldown followed an exponential curve that featured a decay time of 18 hours with an asymptote of approximately 120K.  The cooldown versus time for one of the thermocouples embedded in the winding form is shown in Figure 3-1.

Figure 3-1 - Winding form cooldown versus time

The SRD requirement is for the modular coils to be cooled down to operating temperature (nominally 80K) within 96 hours.  Cooling from 293K to 90K assuming an 85K interior temperature would require a decay time of 25 hours (if an exponential model applied).  The cooldown of C1 was based on cooling the interior and exterior of the shell.  In the stellarator, the space between the modular coil and vacuum vessel (the interior of the shell) will be filled with insulation.  Therefore, the surface area exposed to GN2 will be reduced by more than half.  The decay time should be inversely proportional to the exposed surface area and the convective heat transfer coefficient.  The decrease in surface area will have to be compensated by an increase in the convective heat transfer coefficient.  This will likely require a change from natural (free) convection to forced convection by either improved circulation (via a fan or blower) or increased throughput of GN2.  Flow of GN2 needs to be provided to “dead spaces” in the stellarator core.

The asymptotic (bath) temperature of the cryostat was well above the desired 80K.  This too needs to be addressed in the cryostat cooling system design.  In equilibrium, the cryostat system can be modeled as shown in Figure 3-2.

Figure 3-2 - Cryostat heat balance

Assuming a surface area of 32 m2 for the cryostat and a 6-inch wall of panels with an insulating value of R6 per inch, the heat leak into the cryostat would be approximately 860 W.  If the temperature of the exhaust gas is 120K (the asymptotic temperature calculated for initial cooldown), then a mass flow of 0.0036 kg/s is required.  Two thirds of the heat is removed by evaporating LN2 with the balance removed by the temperature rise in the exhaust gas.

In the stellarator, we want to minimize any temperature rise in the exhaust gas in order to keep the temperature as close to 80K as possible.  This will likely require a large flow of cold (80K or below) purge gas.  Evaporating the LN2 passively from a tank alone may not work because the temperature difference between the cryostat interior and the tank will be so small.  The purge gas could be generated by flowing GN2 through a coil in the LN2 tank.  The temperature of the cryostat interior would be controlled by controlling the flow of the purge gas.  The flow of purge gas should also improve the heat transfer to the modular coil shell.  The ability to introduce purge gas is also desirable for warming up the cold mass.  The one caveat is that we may have to recycle the GN2 throughput in order to limit nitrogen consumption.

When the temperature inside the cryostat approached 130K, 2-phase product was introduced into the coolant channels.  Ultimately, single phase LN2 was circulated through the winding pack which brought the chamber down in temperature to 100K (TC18 in Figure 3-3) in approximately ten (10) hours.  This temperature was well above the 80K temperature envisioned for the coil environment.  Thermocouples embedded in the winding form near the winding pack read as low as 92K (TC3) and 94K (TC2).  The inlet temperature read as low as 83K (TC7) with an outlet temperature of 87K (TC9).  Note that the beneficial effect of cooling the chamber brought about be cooling the winding pack with LN2 will not be manifest (at least not directly) in the stellarator because the winding pack will be thermally insulated.  Note also that there were no measurements of the winding form temperature apart from the two thermocouples embedded deep in the winding form close to the winding pack.  Additional thermocouples should be provided on the winding forms in the stellarator so temperature differences can be monitored.

The temperature of the winding form in the wings was not monitored.  In the stellarator, this is an area of concern.  The plasma-side surface of the wings is thermally insulated.  The outside surface faces, but is not in good thermal contact with the plasma-side surface of the winding form into which it nests.  It may be beneficial, perhaps necessary, to circulate gaseous nitrogen through the coolant tubes in order to cool the wings and also expedite initial cooldown.

Figure 3-3 - Thermocouple readings during initial cooldown

## Coil testing

A series of shots were taken with the coil cold on June 15 and June 16.  Coil currents were increased from 5kA to 36.5kA.  Coil currents were then decreased down to 15kA.  The prescribed waveform was the same for all of the test shots.  There was a 1s linear rise to full current, a 0.2s flattop, and a 1s linear ramp down to zero current.  Intermediate 2kA shots were taken at approximately 10 minute intervals to measure the coil resistance and infer the average winding temperature.  Test shots (above 2kA) were not initiated unless the coil resistance measured in the 2kA shots was at or below 1.8 milli-ohms which corresponds to an average winding temperature of approximately 98K.  The coil was then allowed to warm back to room temperature during which time additional 15kA shots were taken.  The sequence is shown in Table 3-1.  2kA shots and shots in which there were trips are not shown.  All test data is available from the following URL:

http://ncsx.pppl.gov/NCSX_Engineering/R&D_Results/PPPL/C1%20Testing/Index_C1%20testing.htm

The purpose of the test shots is to validate our modeling of coil performance.  If we successfully predict the performance of the C1 coil in the test shots, then we have increased confidence in the predicted performance during stellarator operation.  There are several aspects of coil performance to be modeled, including [1] cooldown between shots; [2] thermal stresses from initial cooldown; and [3] incremental stresses and displacement due to EM loads during a shot.

Table 3-1 - Summary of test shots

| Shot number | Date and time | Max current (kA) | Pre-shot outlet (TC9) temperature (K) |
| --- | --- | --- | --- |
| 121400 | 6/15 2:54:31pm | 5 | 87.2 |
| 121405 | 6/15 3:33:43pm | 15 | 87.6 |
| 121408 | 6/15 3:52:39pm | 25 | 87.6 |
| 121419 | 6/16 9:54:18am | 35 | 92.1 |
| 121439 | 6/16 12:06:43pm | 36.5 | 89.6 |
| 121453 | 6/16 1:27:56pm | 36.5 | 88.9 |
| 121461 | 6/16 2:31:55pm | 36.5 | 88.8 |
| 121468 | 6/16 3:33:33pm | 25 | 88.6 |
| 121471 | 6/16 3:59:03pm | 15 | 88.6 |
| 121537 | 6/23 9:29:30am | 15 | 256.0 |
| 121540 | 6/23 10:14:37am | 15 | 258.2 |

### Cooldown between shots

There are two diagnostics from which we can monitor cooldown between shots.  The first diagnostic is the thermocouple data.  The was a thermocouple mounted on the outside of the winding pack near hole 85 (TC17).  The second diagnostic is the temperature inferred from the 2kA shots run between test shots.

Consider cooldown following Shot 121461 which was a full current (36.5kA) shot.  A plot is shown in Figure 3-4.  The thermocouple mounted on the surface of the winding pack (TC17) starts off with a temperature reading of 83.2K which is approximately equal to the inlet temperature reading 83.8K (TC7).  During a shot, the temperature of the winding pack is estimated to increase by approximately 28K within the 2.2s shot duration.  The temperature of the chill plate under TC17 rises over the next 4 minutes by 5.3K.  Thereafter, the temperature of the chill plates drops with a decay time of approximately 13 minutes.  After 15 minutes, TC17 still reads 85.7K which is 2.5K higher than the initial temperature.  In order to accommodate the soak time to establish the temperature gradients needed to conduct the heat to the coolant and the subsequent thermal decay time, it appears necessary to accept a pre-shot winding pack temperature which is significantly higher than the coolant temperature.

There are two phenomena that are occurring – temperature redistribution and cooling.  The temperature on the surface of the winding pack can be approximated with a simple model per Equation 3-1.

Equation 3-1

.

Ta is the asymptotic temperature to which the winding pack surface would decay and should approximate the local coolant temperature.  T0 is the initial temperature.  T is the increase in the surface temperature in the absence of cooling following a shot.   is the characteristic temperature redistribution rate.  is the characteristic heat removal rate.  With an assumed coolant temperature of 83K (slightly less than the initial temperature of 83.2K), the “best fit” parameters are a T of 9K, a characteristic temperature redistribution time (1/) of 2 minutes, and a characteristic cooling time (1/) of 13 minutes.  Although the adiabatic temperature rise in the copper conductor is calculated to be 28K, the winding form in the vicinity of the winding pack acts as a heat sink as evidenced by the rise in temperatures in winding form thermocouples (TC2 and TC3).  The assumed coolant temperature of 83K is reasonable because more than one hour transpired since the previous full current pulse.  The agreement between the cooldown data following Shot 121461 and the simple model with these parameters is good as shown in Figure 3-5.

Figure 3-4 - Cooldown following Shot 121461

Figure 3-5 - Winding surface temperature following Shot 121461

An ANSYS model of the winding pack was generated to model cooldown between pulses.  The ANSYS model did not include the epoxy shell (of unknown thickness) outside the chill plates to which the thermocouple was attached.  However, it is instructive to compare the thermal decay rate measured at thermocouple and predicted for the chill plates in the vicinity of the thermocouple.  The cooldown between pulses of the chill plates is shown in Figure 3-6 for four points in time.

Figure 3-6 ANSYS modeling of cooldown following Shot 121461

Thermal decay rates along the height of the chill plate were calculated and matched well with the thermal decay rate observed for the thermocouple (TC17) mounted on the epoxy just outside the chill plate, closer to the coolant tubes than the base of the tee.  A comparison of the measured and calculated thermal decay rates ( in Equation 3-1) are shown in Figure 3-7.

Figure 3-7 Comparison of measured and calculated thermal decay rates

The second diagnostic is the average winding temperature inferred from the 2kA shots between test shots.  The data is shown in Figure 3-8.  Clearly, there is significant noise in the measurement and variation during a shot due to current redistribution among the four parallel conductors (even at constant net current).  Shot 121462 was run at 2:40pm (8 minutes after Shot 121461) and registered a resistance in the range of 1.8-2.3 milli-ohms (2.05 milli-ohm median).  Shot 121463 was run at 2:50pm (18 minutes after Shot 121461) and registered a resistance in the range of 1.5-2.0 milli-ohms (1.75 milli-ohm median).  The median temperatures during Shots 121462 and 121463 are calculated to correspond to temperatures of 103.7K and 96.5K respectively.

Figure 3-8 - Winding resistance measurements

The coil resistance was measured manually (outside the cryostat) at 12:30pm prior to any shots.  This measurement has none of the ripple associated with the 2kA shots.  The resistance was measured to be 1.7 milli-ohms which corresponds to an average winding temperature of 89K.  The outlet temperature of the coolant was also measured to be 89K at this time.  If we assume that the asymptotic temperature of the winding pack (Ta) is 89K and the decay time is 13 minutes (as calculated for the winding pack surface), then the temperature rise during Shot 121461 (T) is estimated to be 28K assuming the simple exponential model in Equation 3-2.  The 28K temperature rise is consistent with adiabatic temperature rise predictions.  The definitions in Equation 3-2 are the same as in Equation 3-1 except that the temperature rise is assumed to be instantaneous.

Equation 3-2

15 minutes after Shot 121461, the winding pack temperature is estimated to be 98K, well above the assumed pre-shot temperature of 89K.  In order to cool down in 15 minutes without further thermal ratcheting, the starting temperature would need to be 95K with a coolant temperature of 80K per this simple model.

The ANSYS code was run to determine what temperature the winding pack would ratchet up to assuming an 80K coolant temperature and a 15 minute pulse repetition rate.  The results are shown in Figure 3-9.  The average conductor temperature is predicted to ratchet up to 92K after approximately six shots.  No issues are apparent with starting a shot at this higher operating temperature.

Figure 3-9 Evolution of conductor temperature during continual pulsing

# Strain gage technology

Technical notes from Vishay on strain gage technology can be found at the following URL

http://www.vishay.com/brands/measurements_group/guide/indexes/tn_index.htm

# Reference Tables and Figures

Table 5-1 Thermocouple descriptions

Table 5-2 Strain gage descriptions

Strain gages in gray-scale rows not installed

Figure 5-1 Strain gage data for Shot 121461 for strain gages mounted on the winding form

Figure 5-2 Strain gage data for Shot 1212461 for strain gages mounted on the winding pack

Figure 5-3 Calculation of thermal output for strain gages

# Photographs of the test setup

Figure 6-1 Cryostat carriage in fabrication

Figure 6-2 Cross-section of 4-conductor current feed with fiberglass angle supports

Figure 6-3 Connection of current feed to C1 coil

Figure 6-4 Crimped lugs on current feeds

Figure 6-5 Bus connection to 4-conductor current feed inside thermal transition box

Figure 6-6 Connection of cryostat to facility exhaust

Figure 6-7 Cryostat inside Coil Test Facility

Figure 6-8 C1 coil inside cryostat

Figure 6-9 Restraints on C1 supports

Figure 6-10 Instrumentation of jumper assembly

Figure 6-11 Strain gages at Clamp 68 - Side B

Figure 6-12 Casting strain gages at Clamp 68 - Side B

Figure 6-13 Strain gages at Clamp 50 - Side B

Figure 6-14 Strain gage at Clamp 42 - Side A

Figure 6-15 Strain gage (SG15) near lead block

Figure 6-16 Winding pack strain gage (dummy) at Clamp 7 - Side B

Figure 6-17 Winding pack thermocouple (TC17) under glass wool

# Footnotes

G. Gettelfinger, private communication