NCSX Coil Test, Sot 118103 Filtered Coil Resistance, Box Car 100 Samples. No Halmar#2 Data

Calculated Coil Resistance in mOhms. White=Chan#1/Halmar#1, Blue= Chan#2/Halmar#1

Offset and Gain Adj. Coil Voltages – Unfiltered

2000 Samples per Sec. Voltage Peak transition in 3 samples or 1.5 mSec

Pre-Voltage Probe Installation. Voltage Probes located where indicated. 1st or Chan #1 right most studs, 2nd or Chan #2 left most studs.

Filtered and Offset Corrected Coil Current. No Halmar #2 Data.

Halmar #2 Data, Filtered (Box Car – 100 samples) and offset corrected.