NCSX

Design Basis Analysis

Vacuum Vessel Support Rod Analysis

NCSX-CALC-12-004-dA

02 November 2004

Prepared by:

_______________________________________

P. L. Goranson, ORNL

I have reviewed this calculation and, to my professional satisfaction, it is properly performed and correct.  I concur with analysis methodology and inputs and with the reasonableness of the results and their interpretation.

Reviewed by:

_______________________________________

K. Freudenberg Engineer

Introduction

The Vacuum Vessel Subassembly (VVSA) utilizes six threaded support rods to suspend the VVSA from the interior of the Modular Coil (MC) shell structure. Lateral supports mounted on the Neutral Beam Transition Duct position the VVSA and react off-center loads to the MC struructure. Two internally threaded bosses are built into each of the VVSA assemblies near the Neutral Beam. Corresponding boss features are built into the shell such that the supportr rods will be vertical when the MC Shell and VVSA are at room temperature.

VV wall stresses have been analyzed by a separate DAC.

Design Description – Per figure

A threaded clevis screws into boss at the VV end.

A commercial rod end and spherical bearing attaches rod to clevis.

A nut and self-aligning washer on the threaded rod supports the load at the MC.

Performance Requirements and Criteria

No credit is given for lower hangers which could be used to preload the VV and reduce dynamic loads.

A safety factor of three based on ultimate is acceptable.

Methodology

Hand calculations were done to determine simple tensile and shear stresses in the components based on static gravity and magnetic loads.

Assumptions

- Rod thread

3/4-10UNC

Stress area = 0.313 in^2

Minor dia = 0.6309 in

The design utilizes a minimum thread engagement of 1.5 diameters, which assures full tensile capability for the rod, therefore, thread shear is not an issue and is not analyzed here.

2. Vessel weight = 24000 lbs

3. All six supports are loaded equally in pure tension.

4. Material properties

6Al-4V titanium alloy.properties from MIL-T-9047

Yield is 150 ksi

Tensile is 160 ksi

Yield at 350 C is 60%

Tensile at 350 C is 70%

Yield at 80 K is 160%

Tensile at 80 K is 155%

Inconel 625 properties from AMS 5666

Tensile at room is 120 ksi, 105.6 ksi at 350 C.

Yield at room is 60 ksi, 42 ksi at 350 C.

G-10 insulation

Material comprssive strength is rated at 60ksi.

5. VV is never at 350 C during plasma operation. Reduced allowables due to temperature are not applicable during magnetic loading.

6. Dynamic disruption load, from Dahlgren, is two times static load.

Results

1. Tensile stress at thread root.

Tensile stress(static) = 12800 psi

Dynamic tensile stress = 25600 psi

Safety factor, based on ultimate, during disruption is 6.25.

- Clevis threads

Stress is same as in rod but strength of of I625 is less than titanium alloy.

Safety factor, based on ultimate during disruption and room temperature is 4.7.

Safety factor based on ultimate during static load and 350 C is 3.28.

- Weld joint in VV boss.

Boss dia = 2 in

Weld depth = 0.375 in

Weld area = 2.36 in^2

Assume:

Weld metal is same as annealed Inconel 625 base metal properties

Full penetration weld through 3/8 wall.

Allowable is based on AWS welding allowable for carbon steel welding, 11200 psi, a much more conservative value in this case.

Results

Shear stress

Sstatic = 1698 psi

Sdynamic = 3395 psi

Safety factor is 3.3 during disruption, based on AWS allowable.

4. G-10 Insulation Bearing Stress

A G-10 electrical insulation is used under the spherical washer seat

OD = 2.5", ID = 1.0"

Temperature ranges from room temperature down to 80K.

Static compressive stress = 318 psi

5. Rod End

Rod end is a commercial design rated at 29300 lbs each.

Summary

The critical component in the design will be the weld between the boss and the VV. The vessel total suspended weight may be safely increased by 2400 lbs, to 26400 lbs in later upgrades.

A means, i.e. Bellville washers, must be used to assure equal loading of the rods.

# Text boxes

Controlled Document

THIS IS AN UNCONTROLLED DOCUMENT ONCE PRINTED.

Check the NCSX Engineering Web prior to use to assure that this document is current.