COGNIZANT INDIVIDUAL:	Michael Kalish

ECN TITLE:  TF Coil Manufacturing Upgrades

ASSOCIATED ECP:  None

CC/WP/Job:	9450 1*** 1361	     	AREA OR PROJECT:    NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __________________________________

(Signature indicates that no Work Planning form is required.)

If non-concurrence or associated with a work planning form, enter the WP Number:

| DRAWING(S) AFFECTED NUMBER: | Current Revision | TITLE |
| --- | --- | --- |
| SE131-085 | 2 | TF Coil Nose Casting Machining |
| SE131-035 | 1 | TF Coil Winding Assembly |
| SE131-003 | 1 | TF Coil Final Assembly |
| SE131-053 | 1 | TF Coil Lead Long Bent Right |
| SE131-081 | 1 | TF Coil Lead Long Right (Unbent) |

DESCRIPTION OF CHANGE: (State Drawing No., Zone/Group, or List Attachments) Changes that were requested by ETI to enhance manufacturability (See Attached ETI memo): Add Notch to the front edge of the Wedge Casting to make the glass tape wrap underflush on SE131-085. Add .406dia x .50deep tooling holes to front and back of wedge on SE131-085 per markup. Remove 3/8-16 tooling holes in four places on SE131- 085. Add 1/8” radius at the top and bottom edges of the Wedge Casting sheet 1 of SE131-085, Zones K4 and B4. Update the assembly drawing SE131-035 to show the boot at the top and the bottom of the Wedge Casting Blended in. Change note 1 on assembly drawing SE131-003 sheet 3 to reflect 6 inspection locations. Add 1” wide .040” deep fly cut on front surface of wedges at 6 inspection locations on final assembly drawing SE131-003. PPPL Initiated Changes: Update the TF Flag Drawings (SE131-053 and SE131-081) to correct flat pattern so that it matches the model for Long Lead Right (Unbent) SE131-081 and Long Lead Right Bent SE131-053. Change Reference dimension on drawing SE131-035 Sheet 2 in zone C3 From: 27.428 To: 27.433. In Final Assembly Drawing (SE131-003) add clearance holes for metrology reference points designated in the TF Assembly Specification).

REASON FOR CHANGE: ETI Requested Changes: Notch added to make tape on wedge under flush in VPI mold to enhance manufacturability (SE131-085). Tooling holes .406dia added to hold wedge assembly during final machining of wedge angle (SE131-085). Tooling holes 3/8 dia not required by Everson therefore these were removed (SE131-085). External radius added to wedge to enhance manufacturability of mold which needs an inside radius (SE131-085). The epoxy glass boot which pins the wedge structure in place will be feathered into the ground wrap instead of having a step to enhance manufacturability of the VPI mold. Number of inspections points were changed because one inspection point fell under the wrap (SE131-035). A .04” fly cut was added at the inspection points to provide a precise surface for the inspection fixture (SE131-003).

REASON FOR CHANGE (continued): PPPL Initiated Changes: Mistake corrected in flat pattern and bent TF Flag drawings to agree with model (se131-053 AND se131-081). Reference Dimension Corrected on SE131-035. Access holes on front face of wedge are added for metrology and assembly purposes (SE131-003).

ENGINEERING CHANGE NOTICE APPOVALS: DATE: 11/14/2006

COGNIZANT INDIVIDUAL MAKING THE CHANGE:

RESPONSIBLE LINE MANAGER:

RLM COMMENTS: Update drawings immediately.