PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 4945R1

COGNIZANT INDIVIDUAL:	Paul Goranson

ECN TITLE:  Incorporation of changes detailed under Addendum letter 3-1 and 3-3.

ASSOCIATED ECP:  019

CC/WP/Job: 9450-1***-1250			     	AREA OR PROJECT:    NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __________________________________

(Signature indicates that no Work Planning form is required.)

If non-concurrence or associated with a work planning form, enter the WP Number: 1096

| DRAWING(S) AFFECTED NUMBER: | NEW Revision | TITLE |
| --- | --- | --- |
| SE122-019 | Rev 2 | Vacuum Vessel Port 12 Seal Retainer |
| SE120-004 | Rev 2 | Vacuum Vessel Period Inspection and Leak Check Assembly |
| SE120-003 | Rev 1 | Vacuum Vessel Period Assembly and Removed Port Extensions |
| SE121-014 | Rev 1 | Vacuum Vessel Spacer Weldment |
| SE122-104 | Rev 1 | Vacuum Vessel Port 12 Cover Test Flanges Weldment |
| SE122-112 | Rev 1 | Vacuum Vessel 12 Inch Cover Test Flange Detail |
| SE122-149 | Rev 1 | Vacuum Vessel Port 4 Cover Test Flange Weldment |
| Continued on Back |

PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 4945R1

DESCRIPTION OF CHANGE: (State Drawing No., Zone/Group, or List Attachments) Addendum letter 3-1 SE122-104 Relax 0.625”hole depth tolerance to two places, per vendor request. SE122-019 Change 0.271 typical dimension in zone G4 to reference dimension, per vendor request. SE120-004, sht 16 Add weld detail to Dome feature. Addendum letter 3-3 SE120-004, shts 5, 13, and 15. Add alternate design port extension weld configuration Option #1 on ports 4 and 12, per request by vendor. SE120-003, sht2. Add note relaxing inward tolerance in zone around Ports 4A, 4B, 12A, and 12B per request by vendor. SE120-004, sht 9 and sht 19, SE122-104, SE122-112, SE122-149, SE121-014. Add note to drawings to change pumpout ports to optional per vendor discretion.

REASON FOR CHANGE: To incorporate drawing changes initiated by Addendum 3-1 and 3-3.

ENGINEERING CHANGE PROPOSAL: ECP-019 DATE: 1/25/2005

COGNIZANT INDIVIDUAL MAKING THE CHANGE:

RESONSIBLE LINE MANAGER:

Note:  Rev 1 removed drawing SE120-005 shts 1-3 since no change needed.

COGNIZANT INDIVIDUAL:	Paul Goranson

ECN TITLE:  Incorporation of changes detailed under Addendum letter 3-1 and 3-3.

ASSOCIATED ECP:  019

CC/WP/Job:			     	AREA OR PROJECT:    NCSX

| DRAWING(S) AFFECTED NUMBER: | NEW REV. | TITLE |
| --- | --- | --- |
| SE122-104 | 2 | Vacuum Vessel Port 12 Cover Test Flanges Weldment |
| SE122-112 | 1 | Vacuum Vessel 12 In Cover Test Flange Detail |
| SE122-149 | 1 | Vacuum Vessel Port 4 Cover Test Flange Weldment |