PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 4994

COGNIZANT INDIVIDUAL:	D. Williamson

ECN TITLE:  Revise MCWF Leads Interface Features

ASSOCIATED ECP:  ECP-033

CC/WP/Job:		1403	     	AREA OR PROJECT:    NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __________________________________

(Signature indicates that no Work Planning form is required.)

If non-concurrence or associated with a work planning form, enter the WP Number:

| DRAWING(S) AFFECTED NUMBER: | NEW Revision | TITLE |
| --- | --- | --- |
| SE141-114 | 4 | Modular coil winding form, Type-A |
| SE141-115 | 4 | Modular coil winding form, Type-B |
| SE141-116 | 5 | Modular coil winding form, Type-C |
| Continued on Back |

DESCRIPTION OF CHANGE: (State Drawing No., Zone/Group, or List Attachments) SE141-114 – Sheet 7, Quad D2, A3-5: Revised lead block detail and section views; revised dimension scheme for mounting pad, resulting in reduction of mounting pad height. SE141-115 – Sheet 7, Quad D5, B4-6 and Sheet 4, Quad B7 Revised lead block detail and section views; revised dimension scheme for mounting pad, resulting in reduction of mounting pad height. Added chamfer to inboard TF support. SE141-116 – Sheet 8, Quad D8, B5-7 Revised lead block detail and section views; revised dimension scheme for mounting pad, no change in pad height.

PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 4994

REASON FOR CHANGE: Due to re-design of lead blocks assembly, it is necessary to change the slot length from 6.38-in to 7.5-in and the slot width from 1.5-in to 1.5625-in. The location and dimensions of four tee base tapped holes w/ spotface are also changed to conform to the new design. The mounting pad dimensioning scheme was revised, resulting in a slight change in the pad height for the Type-A and –B winding forms.

ENGINEERING CHANGE PROPOSAL: ECP-033 DATE: 6/10/05

COGNIZANT INDIVIDUAL MAKING THE CHANGE: D. Williamson

RESONSIBLE LINE MANAGER: B. Nelson

PPPL ENGINEERING CHANGE NOTICE (ECN)	ECN #

(Continuation Page)

| DRAWING(S) AFFECTED NUMBER: | NEW REV. | TITLE |
| --- | --- | --- |