PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 5026

COGNIZANT INDIVIDUAL:	D. Williamson

ECN TITLE:  MCWF Type-C Revision Following C1 Inspection

ASSOCIATED ECP:  ECP-038

CC/WP/Job: 1403			     	AREA OR PROJECT:    NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE:__________________________________

(Signature indicates that no Work Planning form is required.)

If non-concurrence or associated with a work planning form, enter the WP Number:

| DRAWING(S) AFFECTED NUMBER: | NEW Revision | TITLE |
| --- | --- | --- |
| SE141-103 | 3 | MOD COIL WINDING FORM ASM TYPE-C |
| SE141-078 | 2 | POLOIDAL BREAK SHIM ASM TYPE-C |
| SE141-116 | 7 | PRODUCTION WINDING FORM TYPE-C |
| DS141-036 | 2 | STUD, 1.375 DIA x 9.5 LG |
| DS141-060 | 1 | NUT, 1.375-6UNC 12 PT HEX |
| DS141-079 | N/A | WASHER, 2.75 OD x 1.66 ID x 0.5 THK |
| SE141-137 | 0 | MCWF POL BREAK BEARING PLATE |
| SE141-138 | 0 | MCWF POL BREAK BEARING PLATE |

DESCRIPTION OF CHANGE: (State Drawing No., Zone/Group, or List Attachments) See RFD-14-009 attachment, “Meeting notes, review of MCWF C1 at PPPL, 10/14/2005”, for detailed sketches depicting changes. Drawing DS141-079 is no longer used by the modular coil winding form assembly. Table of changes from the attachment follows: Item Drawing Sheet Zone Issue Resolution 1 SE141-103 1 2 C2 D5 Washer not suitable for thin flange, required bolt preload. Replace washer with bearing plates, SE141-137 and SE141-138. 2 SE141-078 1 F7 Shim edges are flush with insulator, making it difficult to seal for VPI. Also, potential for voltage breakdown. Add instruction to chamfer all shim edges 1/16”. 3 DS141-036 (stud) DS141-060 (nut) 1 1 N/A N/A Material specification is incorrect (both drws) and stud length must match revised drawing to accommodate bearing plates. Revise material to ASTM A453, Grade 660B. 4 SE141-116 5 E8 Tapped and thru hole were not positioned according to latest model/drawing revision. Adopt latest rev for hole position, change tapped hole from thru to 1.25” blind due to flange radius. 5 SE141-116 5 F7 Spherical seat size tolerance +/- .01 is not suitable for intended use. Change size tolerance to +.002/-.003. Pilot hole up to 3/8” is acceptable. Lap finish to final size tolerance of +.002/-.000. 6 SE141-116 6 D3 Poloidal break edge is flush with insulator. Add instruction for 1/16 chamfer all surfaces and edges of break. 7 SE141-116 9 C7 F3 Cooling inlet/outlet thru hole diameter is too small, and one hole interferes with flange. Revise location and diameter of the interfering hole and the diameter of the other seven holes. 8 SE141-116 10 D2 As-cast tolerance is not suitable over a small area where wing of adjacent coil overlaps. Revise profile tolerance to +.05 / -.1 over area defined by IGES surface. 9 SE141-116 NEW N/A Four thru holes to be added for cooling line inlet/outlet at poloidal break. Add drawing view.

REASON FOR CHANGE: Inspection of MCWF C1 identified several issues requiring resolution and/or clarification. Some were manufacturing and some were design errors.

ENGINEERING CHANGE PROPOSAL: ECP-038 DATE: 10/24/2005

COGNIZANT INDIVIDUAL MAKING THE CHANGE: D. Williamson

RESONSIBLE LINE MANAGER: B. Nelson