PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 5130

COGNIZANT INDIVIDUAL: Paul Goranson

ECN TITLE:  Heating and Cooling System Saddle Loop Design Modifications

ASSOCIATED ECP:  None

CC/WP/Job: 9450-****-1203			     	AREA OR PROJECT:    NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __________________________________

(Signature indicates that no Work Planning form is required.)

If non-concurrence or associated with a work planning form, enter the WP Number:

| DRAWING(S) AFFECTED NUMBER: | NEW Revision | TITLE |
| --- | --- | --- |
| SE123-049 | 1 | Vacuum Vessel Heating/Cooling Heating Cooling ASM Assembly |
| SE123-052 | 3 | Vacuum Vessel Heating/Cooling Heating Cooling Grafoil Gasket Detail |
| SE123-053 | 3 | Vacuum Vessel Heating/Cooling Heating Conductor Detail |
| SE123-054 | 3 | Vacuum Vessel Heating/Cooling Heating Strap Detail |
| SE123-056 | 1 | Vacuum Vessel Heating/Cooling Heating Tube Retainer Washer |

PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 5130

DESCRIPTION OF CHANGE: (State Drawing No., Zone/Group, or List Attachments) SE123-049 Update models and BM to remove Brazette Reducer fitting which will not be required SE123-052 Changed dimensions of gasket. SE123-053 Changed conductor design to accommodate single tracing hose. SE123-054 Changed strap material thickness and geometry to permit increase loading. SE123-056 Changed material to SS.

REASON FOR CHANGE: To accommodate changes in tracing mount design resulting from R&D testing.

ENGINEERING CHANGE PROPOSAL: N/A DATE: 5/16/2006

COGNIZANT INDIVIDUAL MAKING THE CHANGE:

RESONSIBLE LINE MANAGER:

RLM Comments: Changes have been incorporated into the drawings.

PPPL ENGINEERING CHANGE NOTICE (ECN)	ECN #

(Continuation Page)

| DRAWING(S) AFFECTED NUMBER: | NEW REV. | TITLE |
| --- | --- | --- |