PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 5158

COGNIZANT INDIVIDUAL:	D. Williamson

ECN TITLE:  Revise surface profile tolerance for Type-A MCWF

ASSOCIATED ECP:  None

CC/WP/Job:	1403		     	AREA OR PROJECT:    NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: _B. Nelson_________________________

(Signature indicates that no Work Planning form is required.)

If non-concurrence or associated with a work planning form, enter the WP Number:

| DRAWING(S) AFFECTED NUMBER: | NEW Revision | TITLE |
| --- | --- | --- |
| SE141-114 | 8 | Type-A Modular Coil Winding Form |
| Continued on Back |

DESCRIPTION OF CHANGE: (State Drawing No., Zone/Group, or List Attachments) SE141-114-R8, SHT-10, QUAD-D6 Change surface profile tolerance for selected surfaces from +/-.25 to +0/-.25.

PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN #5158

REASON FOR CHANGE: Surfaces of wing pocket coincide with riser placement and thus have stock thickness beyond the “as-cast” profile tolerance. A tolerance change for selected surfaces will ensure clearance with the mating Type-B coil. Additional inspection point data will also be provided.

ENGINEERING CHANGE PROPOSAL: NONE DATE: 8/15/06

COGNIZANT INDIVIDUAL MAKING THE CHANGE: D. Williamson

RESONSIBLE LINE MANAGER: B. Nelson