PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 5185

# COGNIZANT INDIVIDUAL:	David Williamson

# ECN TITLE:	Flange Hole Counterbore Clearance Envelope and Type-B Post Mod

# CC/WP/Job:	9450-1***-1411	                          AREA OR PROJECT:  NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __________________________________

(Signature indicates that no Work Planning form is required.)

# If non-concurrence or associated with a work planning form, enter the WP number:

| DRAWING(S) AFFECTED NUMBER: | Current Revision | TITLE |
| --- | --- | --- |
| SE141-114 | 8 | Type-A Modular Coil Winding Form |
| SE141-115 | 9 | Type-B Modular Coil Winding Form |
| SE141-116 | 8 | Type-C Modular Coil Winding Form |
| Continued on the Back |

PPPL ENGINEERING CHANGE NOTICE (ECN)	ECN # 5185

DESCRIPTION OF CHANGE: (state drawing no., zone. group, or list attachments) SE141-114, -115, -116, Sht-4, 5 -The clearance requirements for all flange back spot faces and for all the remaining winding forms (MCWFs C-6, B-3 through B-6, and A-4 through A6) shall be a 3" diameter cylinder 3" high from the spot face surface. The blend-in radius at the upper extent of this machined area shall be 1/4". SE141-115, Sht-8, Quad-B3 - For Type-B MCWF, a clearance dimension of 9.00 +/-.05-in is defined between the center of the lead block mounting pad and the support post. Clearance envelope height extends through the post as required. REASON FOR CHANGE: The CAD model of the counterbore envelope, 3-in dia x 3-in length with a spherical radius, is not large enough to provide adequate fastener clearance in heavy stocked areas of the casting. There is approx .5-in stock on all sides of the B1 and B2 support posts, which prevents mounting of the leads terminal asm.

ENGINEERING CHANGE NOTICE APPROVALS: DATE: 11/07/2006

COGNIZANT INDIVIDUAL MAKING CHANGE:

DESIGN RESPONSIBLE LINE MANAGER: RLM Comment: Dwg SE141-115 has two RFDs pending and must be revised.

MANUFACTURING RESPONSIBLE LINE MANAGER: