# COGNIZANT INDIVIDUAL:  John Edwards

# ECN TITLE:	Horse Collar Weldment

# CC/WP/Job:	9450-1***-1810                           AREA OR PROJECT:  NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __________________________________

(Signature indicates that no Work Planning form is required.)

# If non-concurrence or associated with a work planning form, enter the WP number:

| DRAWING(S) AFFECTED NUMBER: | Current Revision | TITLE |
| --- | --- | --- |
| SE121-004 | 0 | VVSA Assembly Station 1 |

# COGNIZANT INDIVIDUAL:  John Edwards

# ECN TITLE:	Horse Collar Weldment

# CC/WP/Job:	9450-1***-1810                           AREA OR PROJECT:  NCSX

DESCRIPTION OF CHANGE: (state drawing no., zone. group, or list attachments) SE121-004 (Section C-C) – add a couple of small Inconel splice plates to close the gap (~ 1/4 “). REASON FOR CHANGE: Part 6 doesn't fit properly because the port 12 extensions are oversize. We can grind part 6, but that will be costly. It would be much cheaper to add a couple of small inconel splice plates to close the gap (about 1/4"). See attached sketch.

ENGINEERING CHANGE NOTICE APPROVALS: DATE: 11/14/2006

COGNIZANT INDIVIDUAL MAKING CHANGE:

RESPONSIBLE LINE MANAGER:

RLM Comments: Update drawing immediately.