NCSX ENGINEERING CHANGE NOTICE (ECN)   ECN # 5244-r1

# COGNIZANT INDIVIDUAL:	D. Williamson

# ECN TITLE:	 MC FLANGE BOLT ASM

# CC/WP/Job:	1421	                           AREA OR PROJECT:  NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __________________________________

(Signature indicates that no Work Planning form is required.)

# If non-concurrence or associated with a work planning form, enter the WP number: 1096

| DRAWING(S) AFFECTED NUMBER: | Current Revision | TITLE |
| --- | --- | --- |
| SE140-190 | 1 | MCWF FLANGE STUD KITS |
| SE140-191 | 0 | MCWF FLANGE STUDS |
| SE140-192 | 1 | MCWF INSULATING WASHERS AND SLEEVES |
| SE140-193 | 1 | MCWF WASHER |

NCSX ENGINEERING CHANGE NOTICE (ECN)	ECN # 5244

# COGNIZANT INDIVIDUAL:		D. Williamson

# ECN TITLE:	 MC FLANGE BOLT ASM

# CC/WP/Job:	   1421                                            AREA OR PROJECT:  NCSX

DESCRIPTION OF CHANGE: (state drawing no., zone. group, or list attachments) SE140-190: DELETED 12PT NUT AND SHIM BUSHING. ADDED SUPERNUT, F/N 11 AND WASHER, F/N 8. ADDED SLEEVE, F/N 6. ADDED ADHESIVE, F/N 16 AND INS SHEET. ADDED GRINDING NOTE AND ADDITIONAL INSULATEING METHODS ON SHT 2. ADDED OPTIONAL THRU BOLT CONFIGURATION. SE140-191: LENGTH 6.25 WAS 7.50, 8.00 WAS 10.50. CHANGED THREAD CLASS TO 2A. ADDED REQUIREMENT FOR ROLLED THREADS. SE140-192: ADD G-10CR SLEEVE F/N2 3.00OD X 2.875 ID TUBE SE140-193: REVISED MATERIAL FOR UNSN07718 OR UNS R56400 REASON FOR CHANGE: FEEDBACK FROM FIELD MEASUREMENTS AND ASM TRIALS.

ENGINEERING CHANGE NOTICE APPROVALS: DATE: 4/26/07

COGNIZANT INDIVIDUAL MAKING CHANGE: D. Williamson

RESPONSIBLE LINE MANAGER: Update Drawings Immediately Defer Update and Use ECN Stamp Other Comments: