# COGNIZANT INDIVIDUAL:  Paul Goranson

# ECN TITLE:	 Alternate Weld Detail

# CC/WP/Job:	9401-1***-1810	                           AREA OR PROJECT:  NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __________________________________

(Signature indicates that no Work Planning form is required.)

# If non-concurrence or associated with a work planning form, enter the WP number:  1350

| DRAWING(S) AFFECTED NUMBER: | Current Revision | TITLE |
| --- | --- | --- |
| SE121-009 | 0 | VVSA1 Assembly Station 1 Phase 3 |

DESCRIPTION OF CHANGE: (state drawing no., zone. group, or list attachments)

See Detail D for details.  This change is being generated to enable orbital welding vs. Tig welding for connecting heating and cooling tubes on VV segments.

REASON FOR CHANGE:  The option to utilize orbital welding will give a better result and be less expensive.

# COGNIZANT INDIVIDUAL:	Paul Goranson

# ECN TITLE:	 Alternate Weld Detail

# CC/WP/Job:	9401-1***-1810                                         AREA OR PROJECT:  NCSX

ENGINEERING CHANGE NOTICE APPROVALS: DATE: 5/4/2007

COGNIZANT INDIVIDUAL MAKING CHANGE:

RESPONSIBLE LINE MANAGER: Update Drawings Immediately Defer Update and Use ECN Stamp Other Comments: Show detail on drawing as per stamp