PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 5283

COGNIZANT INDIVIDUAL: Paul Goranson

ECN TITLE: Incorporation of Design Change to Vacuum Vessel Supports

ASSOCIATED ECP:  none

CC/WP/Job: 1204			     	AREA OR PROJECT:    NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __________________________________

(Signature indicates that no Work Planning form is required.)

If non-concurrence or associated with a work planning form, enter the WP Number: 1191

| DRAWING(S) AFFECTED NUMBER: | Revision | TITLE |
| --- | --- | --- |
| SE124-051 | 0 | Vertical Upper Support Assembly |
| SE124-014 | 0 | Vertical Support Rod End, Female |
| SE124-034 | 0 | Vertical Upper Support Spherical Nut |
| SE124-037 | 0 | Vertical Upper Support Stud |

PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 5283

DESCRIPTION OF CHANGE: (State Drawing No., Zone/Group, or List Attachments) SE124-051 – change tolerance positions to reflect as-built conditions of the support bosses. SE124-014 – add locking feature to rod end. SE124-034 – add locking feature to nut. SE124-037 – delete drawing from assembly and Bill of Material List New Drawings – add parts to drawing assembly and Bill of Material List: SE124-075 Vertical Upper Support Stud SE124-076 Vertical Upper Support Spacer Detail SE-124-079 Vertical Upper Support Washer, Belleville SE124-082 Vertical Upper Support Washer, Belleville

REASON FOR CHANGE: SE124-051 A design change is required to accommodate out of tolerance positions of the support bosses on the Vacuum Vessel. SE124-014 and SE124-034 – A locking feature is required to prevent loosening of the support rods. SE124-037 – replaced by SE124-075 New drawings needed to reflect as-built details

ENGINEERING CHANGE PROPOSAL: N/A DATE: December 4, 2007,

COGNIZANT INDIVIDUAL MAKING THE CHANGE:

RESONSIBLE LINE MANAGER: