PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 5355

# COGNIZANT INDIVIDUAL:  T. Brown

# ECN TITLE:	MCWF Support Cart Weldments

# CC/WP/Job:	9450-1***-1803	AREA OR PROJECT:  NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __________________________________

(Signature indicates that no Work Planning form is required.)

# If non-concurrence or associated with a work planning form, enter the WP number:  _______

| DRAWING(S) AFFECTED NUMBER: | Current Revision | TITLE |
| --- | --- | --- |
| SE186-330 | 0 | MCWF Support Cart Weldments |
| SE185-315 | 0 | MCWF Half Period Lifting Fixture Mtg Brkt Weldments |
| Continued on back. |

DESCRIPTION OF CHANGE: (state drawing no., zone. group, or list attachments)

SE186-330: Revise weld callouts; “GTAW” replaced with “GMAW OR FCAW”; “SMAW” specified where space is restrictive. Revise parts callout in field of drawing, Sheet 3, Parts 10 and 11.

SE185-315: Add “TYP” to 3 inch bevel dimension, Part 30, Sheet 6.

# REASON FOR CHANGE:

# SE186-330: Manufacturer change request. Part callouts for 10 and 11 were reversed.

# SE186-315: Added for clarity of intent of design.

ENGINEERING CHANGE NOTICE APPROVALS	:		DATE: May 8, 2008

# COGNIZANT INDIVIDUAL MAKING CHANGE:

# RESPONSIBLE LINE MANAGER: