# COGNIZANT INDIVIDUAL:		Mike Cole

# ECN TITLE:	Port 12 Boot Revision to Allow Installation over Cryostat Flange.

# CC/WP/Job:		 /1806                          AREA OR PROJECT:  NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __Phil Heitzenroder

(Signature indicates that no Work Planning form is required.)

# If non-concurrence or associated with a work planning form, enter the WP number:

| DRAWING(S) AFFECTED NUMBER: | Current Revision | TITLE |
| --- | --- | --- |
| SE122-401 | 0 | PORT 12 WINDING FORM SEAL ASSY |
| SE122-405 | 0 | PORT 12 SEAL BOOT ASSY |
| Continued on the Back |

DESCRIPTION OF CHANGE: (state drawing no., zone. group, or list attachments) SE122-401 ADDED ITEM #8 AND NOTE #4. SE122-405 CHANGED ISO VIEW AND ADDED NOTE "SEAM NOT CLOSED UNTIL INSTALLATION" REASON FOR CHANGE: SE122-401 – To allow boot to slip over cryostat flange and be sewed or stapled after installation. SE122-405 – To fabricate boot without seaming edge at drawstring.

ENGINEERING CHANGE NOTICE APPROVALS: DATE: June 30, 2008

COGNIZANT INDIVIDUAL MAKING CHANGE:

RESPONSIBLE LINE MANAGER: Update Drawings Immediately Defer Update and Use ECN Stamp Other Comments: