# COGNIZANT INDIVIDUAL:		Mike Cole

# ECN TITLE:	Vacuum Vessel Support Rods

# CC/WP/Job:		 /1806                          AREA OR PROJECT:  NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __Phil Heitzenroder____

(Signature indicates that no Work Planning form is required.)

# If non-concurrence or associated with a work planning form, enter the WP number:

| DRAWING(S) AFFECTED NUMBER: | Current Revision | TITLE |
| --- | --- | --- |
| SE124-051 | 1 | VERTICAL UPPER SUPPORT ASSEMBLY |
| SE124-054 | 0 | VERTICAL LOWER SUPPORT ASSEMBLY |
| SE124-055 | 0 | VERTICAL SUPPORT CLEVIS |

DESCRIPTION OF CHANGE: (state drawing no., zone. group, or list attachments) SE124-051 CHANGED HAIRPIN TO COTTER PIN SE124-054 CHANGED HAIRPIN TO COTTER PIN SE124-055 3/4-10UNC WAS 3/4-16UNF REASON FOR CHANGE: SE124-051 – To eliminate the possibility retaining pin from slipping off. SE124-054 – To eliminate the possibility retaining pin from slipping off. SE124-055 – To match threads to the bosses on the vacuum vessel. Per NCR# 3664

ENGINEERING CHANGE NOTICE APPROVALS: DATE: 7/18/2008

COGNIZANT INDIVIDUAL MAKING CHANGE:

RESPONSIBLE LINE MANAGER: Update Drawings Immediately Defer Update and Use ECN Stamp Other Comments: