PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # _4882____

COGNIZANT INDIVIDUAL:	Paul Goranson (ORNL)

ECN TITLE:	Modification to Seals on Spool Piece and End Piece for Vacuum Vessel R&D

CC/WP/Job:	1203-405	AREA OR PROJECT:    NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __________________________________

(Signature indicates that no Work Planning form is required.)

If non-concurrence or associated with a work planning form, enter the WP number:  _______

| DRAWING(S) AFFECTED NUMBER: | NEW Revision | TITLE |
| --- | --- | --- |
| SE1203-001 | 1 | WELD JOINT ASSEMBLY FOR REFERENCE ONLY |
| SE1203-002 | 1 | SPOOL PIECE MACHINING |
| SE1203-003 | 1 | END PIECE MACHINING |
| SE1203-004 | 1 | SPOOL PIECE STOCK WELDMENT |
| SE1203-005 | 1 | END PIECE STOCK WELDMENT |
| Continued on back. |

DESCRIPTION OF CHANGE: (state drawing no.,zone/group, or list attachments)

SE1203-001 Updated to show changes SE1203-002 Mating grooves changed, filet weld removed, views updated, vent hole details added to sheet 3. SE1203-003 Mating grooves changed, views updated SE1203-004 Filet weld removed, added note 7 SE1203-005 Filet weld removed, added note 7. SE1203-006 Update sections SE1203-007 Update sections, remove fillet weld SE1203-008 Removed SE1203-0011 Added contour tolerance SE1203-0012 Removed SE1203-0015 Tolerances changed SE1203-0016 Changed dimensions SE1203-0017 Changed dimensions

REASON FOR CHANGE:

Vendor recommendation to relax contour tolerances and change the seal from a welded wire to a compliant seal material, resulting in looser tolerance requirements and less distortion in the seal plates.ECP-04-013 approved on July 30, 2004.

ENGINEERING CHANGE NOTICE APPROVALS	:		DATE:

COGNIZANT INDIVIDUAL MAKING CHANGE:

RESPONSIBLE LINE MANAGER:

PPPL ENGINEERING CHANGE NOTICE (ECN)	ECN # _4882____

COGNIZANT INDIVIDUAL:	Paul Goranson (ORNL)

ECN TITLE:		Modification to Seals on Spool Piece and End Piece For Vacuum Vessel R&D

CC/WP/Job:	          AREA OR PROJECT:  NCSX

| DRAWING(S) AFFECTED NUMBER: | NEW REV. | TITLE |
| --- | --- | --- |
| SE1203-006 | 1 | SPOOL PIECE SEAL WELDMENT |
| SE1203-007 | 1 | END PIECE SEAL WELDMENT |
| SE1203-011 | 1 | END PIECE & SPOOL PIECE DETAILS |
| SE1203-015 | 1 | STOCK FLANGE DETAIL |
| SE1203-016 | 1 | END PIECE SEAL DETAIL |
| SE1203-017 | 1 | SPOOL PIECE SEAL DETAIL |