PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN #  4961

COGNIZANT INDIVIDUAL:Paul Goranson

ECN TITLE:  Relax tolerances on port extensions

ASSOCIATED ECP:  None

CC/WP/Job: 9450-1***-1250			     	AREA OR PROJECT:    NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __________________________________

(Signature indicates that no Work Planning form is required.)

If non-concurrence or associated with a work planning form, enter the WP Number:

| DRAWING(S) AFFECTED NUMBER: | NEW Revision | TITLE |
| --- | --- | --- |
| SE120-004, sht 1 | 2 | Vacuum Vessel Period Inspection and Leak Check Assembly |
| SE120-004, sht 13 | 2 | Vacuum Vessel Period Inspection and Leak Check Assembly |
| SE120-004, sht 15 | 2 | Vacuum Vessel Period Inspection and Leak Check Assembly |
| Continued on Back |

DESCRIPTION OF CHANGE: (State Drawing No., Zone/Group, or List Attachments) SE120-004, sht 1 Added tolerance of +.125 to port length in general note 6. SE120-004, sht 13 Added tolerance of +.125 to Port 12 dimension and changed dimension from basic to dimensional. SE120-004, sht 15 Added tolerance of +.125 to NB Port and changed dimension from basic to dimensional. Changed dimensions to basic in Section K-K. Added dimension to flange in Detail Y.

PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN #

REASON FOR CHANGE: SE120-004, sht 1 Relax port tolerance per request by vendor. SE120-004, sht 13 Add missing dimension. SE120-004, sht 15 Add missing dimensions. Eliminate conflicting tolerances

ENGINEERING CHANGE PROPOSAL: None DATE:

COGNIZANT INDIVIDUAL MAKING THE CHANGE:

RESONSIBLE LINE MANAGER:

PPPL ENGINEERING CHANGE NOTICE (ECN)	ECN #

(Continuation Page)

| DRAWING(S) AFFECTED NUMBER: | NEW REV. | TITLE |
| --- | --- | --- |