PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 4977

COGNIZANT INDIVIDUAL:	D. Williamson

ECN TITLE:  Modification of existing TRC clamp components

ASSOCIATED ECP:  None

CC/WP/Job:	9450-1***-1406		     	AREA OR PROJECT:    NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __________________________________

(Signature indicates that no Work Planning form is required.)

If non-concurrence or associated with a work planning form, enter the WP Number: 1188

| DRAWING(S) AFFECTED NUMBER: | NEW Revision | TITLE |
| --- | --- | --- |
| SE1405-258P | 1 | Washer, Belleville 0.75OD x .38ID x .03 THK |
| SE1405-261P | 1 | Set Screw, 15/16-20UNF x .38 LG |
| SE1405-263P | 1 | Spherical Washer, 1.5OD x .25 ID |
| SE1405-276 | 1 | Horizontal Bar Clamp |
| SE1405-277 | 1 | Bushing with Spherical Seat |

DESCRIPTION OF CHANGE: (State Drawing No., Zone/Group, or List Attachments) SE1405-258P – Change material to SS (TRC only), add note re magnetic permeability SE1405-261P - Add holes for spanner wrench, change center hole to clearance hole for capture screw SE1405-263P – Change center hole from thru to tapped, change outer diameter to accommodate G11 pad SE1405-276 – Add note for magnetic permeability requirement SE1405-277 – Increase center hole diameter and add note re: magnetic permeability

PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 4977

REASON FOR CHANGE: Redesign to accommodate field changes and recommendations.

ENGINEERING CHANGE PROPOSAL: None DATE: 3/29/05

COGNIZANT INDIVIDUAL MAKING THE CHANGE:

RESONSIBLE LINE MANAGER: B. Nelson