PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 5009 Rev 1

COGNIZANT INDIVIDUAL:	D. Williamson

ECN TITLE:  Revise MCWF Details per Vendor Recommendation

ASSOCIATED ECP:  ECP-035

CC/WP/Job:	1403		     	AREA OR PROJECT:    NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __________________________________

(Signature indicates that no Work Planning form is required.)

If non-concurrence or associated with a work planning form, enter the WP Number:

| DRAWING(S) AFFECTED NUMBER: | NEW Revision | TITLE |
| --- | --- | --- |
| SE141-101 | 2 | MOD COIL WINDING FORM ASM TYPE-A |
| SE141-102 | 2 | MOD COIL WINDING FORM ASM TYPE-B |
| SE141-103 | 2 | MOD COIL WINDING FORM ASM TYPE-C |
| DS141-036 | 1 | STUD, 1.375-6UNC-2A X 9.5 LG |
| SE141-114 | 5 | PRODUCTION WINDING FORM TYPE-A |
| SE141-115 | 5 | PRODUCTION WINDING FORM TYPE-B |
| SE141-116 | 6 | PRODUCTION WINDING FORM TYPE-C |
| DS141-038 | 0 | INSULATING WASHER - OBSOLETE |

DESCRIPTION OF CHANGE: (State Drawing No., Zone/Group, or List Attachments) SE141-101, -102, and -103: SHT-1, QUAD-C3 – Replaced insulating washer, DS141-038, with ins sheet, 26x3x.063 thk SHT-1, QUAD-B1 – Cosmetic only changes to parts list SHT-1, QUAD-F3 – Added notes re hole size, segmentation of sheet insulators SHT-2, QUAD-A6, G3 – Replaced insulating washer with ins sheet SHT-2, QUAD-B1 – Increased bushing length to match as-built configuration SHT-2, QUAD-F6 – Increased stud length to match as-built configuration CONTINUED ON NEXT PAGE SE141-114 and -115: SHT-7, QUAD-B6 – Geom change and note, NO VPI GROOVE AS INDICATED SHT-7, QUAD-B6 – Removed tapped hole w/ spotface, added hole feature and note, FEATURE FOR AXIS DETERMINATION ONLY, MARK LOCATION ON PART SE141-116: SHT-8, QUAD-A6 – Geom change and note, NO VPI GROOVE AS INDICATED SHT-8, QUAD-A6 – Removed tapped hole w/ spotface, added hole feature and note, FEATURE FOR AXIS DETERMINATION ONLY, MARK LOCATION ON PART DS141-036: SHT-1 – Increased stud length to match as-built configuration DS141-038: DRAWING IS OBSOLETE. DO NOT USE.

REASON FOR CHANGE: Fabrication changes recommended by Major Tool.

ENGINEERING CHANGE PROPOSAL: DATE: ECP-035 8/5/05

COGNIZANT INDIVIDUAL MAKING THE CHANGE: D. Williamson

RESONSIBLE LINE MANAGER: B. Nelson