PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 5045

COGNIZANT INDIVIDUAL:	D. Williamson

ECN TITLE:  General Revision, Type-C Winding Form and Stud Weldment

ASSOCIATED ECP:  None

CC/WP/Job:	1403		     	AREA OR PROJECT:    NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __________________________________

(Signature indicates that no Work Planning form is required.)

If non-concurrence or associated with a work planning form, enter the WP Number:

| DRAWING(S) AFFECTED NUMBER: | NEW Revision | TITLE |
| --- | --- | --- |
| SE141-123 | 1 | TYPE-C WINDING FORM AND STUD WELD |
| Continued on Back |

DESCRIPTION OF CHANGE: (State Drawing No., Zone/Group, or List Attachments) Sheet 1, Quad C4 – Replace washer with bearing plates, SE141-137 and -138. Sheet 2, Quad C3 – Change thread size from 3/8-16 to ½-13UNC thru, typ 4 places. Model is correct, but drawing note is not. Sheet 4 – Add views of cooling line inlet/outlet, indicating additional hole detail.

PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN #5045

REASON FOR CHANGE: Modifications result from inspection of C1 casting and operations prior to start of winding.

ENGINEERING CHANGE PROPOSAL: N/A DATE: 11/28/05

COGNIZANT INDIVIDUAL MAKING THE CHANGE: D. Williamson

RESONSIBLE LINE MANAGER: B. Nelson