PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 5066

COGNIZANT INDIVIDUAL:	D. Williamson

ECN TITLE:  Type-C Winding Pack Dimensions and Upper Lead Blocks Mod

ASSOCIATED ECP:  None

CC/WP/Job:	1403		     	AREA OR PROJECT:    NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __________________________________

(Signature indicates that no Work Planning form is required.)

If non-concurrence or associated with a work planning form, enter the WP Number:

| DRAWING(S) AFFECTED NUMBER: | NEW Revision | TITLE |
| --- | --- | --- |
| SE142C-019 | 1 | TYPE-C WINDING PACK DIMENSIONS |
| SE142C-136 | 1 | TYPE-C SIDE-A UPPER LEAD BLOCK |
| SE142C-137 | 1 | TYPE-C SIDE-B UPPER LEAD BLOCK |

DESCRIPTION OF CHANGE: (State Drawing No., Zone/Group, or List Attachments) Revised winding pack and conductor dimensions to match Twisted Racetrack Coil (TRC) measurements. Revised large radius (zone G6) of upper lead block fingers to match as-built configuration. Added slot/chamfer (zone D4) to accommodate flux loop twisted pair wire.

PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN #5066

REASON FOR CHANGE: Correlate Type-C cross-section drawing with TRC observations and data. Revised upper lead blocks to match field changes during assembly.

ENGINEERING CHANGE PROPOSAL: N/A DATE: 1/19/06

COGNIZANT INDIVIDUAL MAKING THE CHANGE: D. Williamson

RESONSIBLE LINE MANAGER: B. Nelson