PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 5067

COGNIZANT INDIVIDUAL: Paul Goranson

ECN TITLE: Incorporation of Changes Authorized by Approve RFDs

ASSOCIATED ECP:  044

CC/WP/Job: 1203			     	AREA OR PROJECT:    NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __________________________________

(Signature indicates that no Work Planning form is required.)

If non-concurrence or associated with a work planning form, enter the WP Number:

| DRAWING(S) AFFECTED NUMBER: | NEW Revision | TITLE |
| --- | --- | --- |
| SE120-004 | 3 | Vacuum Vessel Period Inspection and and Leak Check Assembly |
| SE122-173 | 2 | Vacuum Vessel Port NB Seal Retainer Detail |

DESCRIPTION OF CHANGE: (State Drawing No., Zone/Group, or List Attachments) SE120-004 sheet 18 and 19 - Make mounting holes in bosses true position to Datum B and Datum C only and remove true position callout for datum A. SE122-173 - Change the dimensioning and tolerancing of the retainer to match the o-ring dimensions recommended by the Supplier.

PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 5067

REASON FOR CHANGE: SE120-004 – per approved RFD-12-009, SE120-004 changed to remove unnecessary reference to Datum A. SE122-173 – per approved RFD-12-010, SE122-173 revised to permit grinding the outside profile (maintaining the angle and surface finish) inward to reduce interference created by undersized metal o-ring.

ENGINEERING CHANGE PROPOSAL: N/A DATE: 2/7/2006

COGNIZANT INDIVIDUAL MAKING THE CHANGE:

RESONSIBLE LINE MANAGER:

PPPL ENGINEERING CHANGE NOTICE (ECN)	ECN #

(Continuation Page)

| DRAWING(S) AFFECTED NUMBER: | NEW REV. | TITLE |
| --- | --- | --- |