PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN #  5082

COGNIZANT INDIVIDUAL: Paul Goranson

ECN TITLE:  Elimination of Weld Relief on End Covers

ASSOCIATED ECP:

CC/WP/Job: 1204			     	AREA OR PROJECT:    NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __________________________________

(Signature indicates that no Work Planning form is required.)

If non-concurrence or associated with a work planning form, enter the WP Number:

| DRAWING(S) AFFECTED NUMBER: | NEW Revision | TITLE |
| --- | --- | --- |
| SE 121-014 | See RLM Comment | Vacuum Vessel Spacer Weldment |
| SE 121-091 | See RLM Comment | Vacuum Vessel – Spacer Blank Off Plate Detail |
| SE121-004 | See RLM Comment | Vacuum Vessel Period Inspection and Leak Check Assembly |

DESCRIPTION OF CHANGE: (State Drawing No., Zone/Group, or List Attachments) SE121-014 – elimination of leak checking groove SE121-091 (Zone G-4) – elimination of leak checking groove. SE121-004 (Sheets 4 through 19) – weld symbol for joining the port extension to the vessel.

PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 5082

REASON FOR CHANGE: Requirement originally included to facilitate leak checking by MTM. However, MTM elected another means of leak checking and therefore these grooves are no longer required.

ENGINEERING CHANGE PROPOSAL: DATE: 4/17/2006

COGNIZANT INDIVIDUAL MAKING THE CHANGE:

RESONSIBLE LINE MANAGER:

RLM Comments: This ECN will NOT be immediately incorporated. Rather a stamp will be placed on this drawing as Rev 2-d to SE120-004, Rev 0-b to SE 121-091, and Rev 0-b to SE121-014 to indicate that this ECN is outstanding.