PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 5100

COGNIZANT INDIVIDUAL:	D. Williamson

ECN TITLE:  Revise profile tolerance of Type-B wing pocket

ASSOCIATED ECP:  None

CC/WP/Job:	1403		     	AREA OR PROJECT:    NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __________________________________

(Signature indicates that no Work Planning form is required.)

If non-concurrence or associated with a work planning form, enter the WP Number:

| DRAWING(S) AFFECTED NUMBER: | NEW Revision | TITLE |
| --- | --- | --- |
| SE141-115 | 7 | PRODUCTION WINDING FORM TYPE-B |
| Continued on Back |

DESCRIPTION OF CHANGE: (State Drawing No., Zone/Group, or List Attachments) Per study of as-built dimensions for C1-C4, there is a need to revise the profile tolerance of the wing pocket of the Type-B winding form from +/-.25 to +0/-.12-inch. Reference the attachment, “MC C4 Review – R1.PPT”, T. Brown, 3/27/06.

PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN #5100

REASON FOR CHANGE: Existing Type-C winding forms have positive tolerance on the wing exterior surfaces, relative to the requirements of drawing revision -8. In order to maintain an adequate gap for assembly, the Type-B wing pocket region must be specified with a negative profile tolerance.

ENGINEERING CHANGE PROPOSAL: None DATE: 3/29/06

COGNIZANT INDIVIDUAL MAKING THE CHANGE: D. Williamson

RESONSIBLE LINE MANAGER: B. Nelson