PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 5105

COGNIZANT INDIVIDUAL:	D. Williamson

ECN TITLE:  MATERIAL CHANGE FOR MCWF BEARING PLATES

ASSOCIATED ECP:  None

CC/WP/Job:	1403		     	AREA OR PROJECT:    NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __________________________________

(Signature indicates that no Work Planning form is required.)

If non-concurrence or associated with a work planning form, enter the WP Number:

| DRAWING(S) AFFECTED NUMBER: | NEW Revision | TITLE |
| --- | --- | --- |
| SE141-137 | 2 | TYPE-C SHORT BEARING PLATE DETAIL |
| SE141-138 | 2 | TYPE-C LONG BEARING PLATE DETAIL |
| SE141-139 | 1 | TYPE-B SHORT BEARING PLATE DETAIL |
| SE141-140 | 1 | TYPE-B LONG BEARING PLATE DETAIL |
| SE141-141 | 1 | TYPE-A SHORT BEARING PLATE DETAIL |
| SE141-142 | 1 | TYPE-A LONG BEARING PLATE DETAIL |
| SE141-114 | 7 | PRODUCTION WINDING FORM TYPE-A |
| Continued on Back |

DESCRIPTION OF CHANGE: (State Drawing No., Zone/Group, or List Attachments) SE141-137 thru -142: Material changed from 316 SS to STELLALLOY, the casting material. Ref RFD-14-016. SE141-114, SHEET 9: Thermocouple hole diam changed to .63 for all but last 1-in of depth, which remains at .25-in. Ref RFD-14-017.

PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN #5105

REASON FOR CHANGE: SE141-137 thru -142: Improve magnetic permeability. SE141-114, SHEET 9: Improve machining technique.

ENGINEERING CHANGE PROPOSAL: NONE DATE: 3/31/06

COGNIZANT INDIVIDUAL MAKING THE CHANGE: D. Williamson

RESONSIBLE LINE MANAGER: B. Nelson