PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 5059R3

COGNIZANT INDIVIDUAL:	D. Williamson

ECN TITLE:  MCWF Type-A and –B General Revision incl Bearing Plates

ASSOCIATED ECP:  None

CC/WP/Job:	9450-1***-1403		     	AREA OR PROJECT:    NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __________________________________

(Signature indicates that no Work Planning form is required.)

If non-concurrence or associated with a work planning form, enter the WP Number:

| DRAWING(S) AFFECTED NUMBER: | NEW Revision | TITLE |
| --- | --- | --- |
| SE141-101 | 3 | Mod Coil Winding Form Asm Type-A |
| SE141-102 | 3 | Mod Coil Winding Form Asm Type-B |
| SE141-048 | 2 | Poloidal Break Shim Assembly Type-A |
| SE141-058 | 2 | Poloidal Break Shim Assembly Type-B |
| SE141-114 | 6 | Production Winding Form Type-A |
| SE141-115 | 6 | Production Winding Form Type-B |
| SE141-137 | 2 | MCWF Poloidal Break Bearing Plate Type-C |
| SE141-138 | 2 | MCWF Poloidal Break Bearing Plate Type-C |
| SE141-139 | 0 | MCWF Poloidal Break Bearing Plate Type-B |
| SE141-140 | 0 | MCWF Poloidal Break Bearing Plate Type-B |
| SE141-141 | 0 | MCWF Poloidal Break Bearing Plate Type-A |
| SE141-142 | 0 | MCWF Poloidal Break Bearing Plate Type-A |

PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 5059R3

DESCRIPTION OF CHANGE: (State Drawing No., Zone/Group, or List Attachments) The purpose of this revision is to incorporate changes made to Type-C after C1 delivery into the Type-A and –B drawings: SE141-101, -102 – replaced washer with bearing plates in pol break assembly, revised note #10 regarding thread lubricant, added note #15 regarding bolt torque requirements SE141-048, -058 – added 0.060” – 0.090” edge chamfer. SE141-114, -115 – changed sph seat size tolerance, added edge chamfer, added four additional cooling holes , consistent with changes made to Type-C winding form in ECN-5026, Items #5,6, and 9. SE141-137, -138 – new drawings which describe Type-B bearing plate details. And deleted note referring to magnetic permeability (ECN-5059R3 change). SE141-139, -140 – new drawings which describe Type-B bearing plate details. SE141-141, -142 – new drawings which describe Type-A bearing plate details.

REASON FOR CHANGE: SE141-101, -102 – revised to show bearing plates in poloidal break assembly and additional fastener notes SE141-048, -058 revised to reflect chamfer requirements for Type A and Type B castings similar to that for the Type C castings (SE141-078). SE141-114, -115 revised to make identical changes to cooling holes and tolerances as was done for Type C (SE141-116). SE141-137, -138 revised to delete the note relative to the magnetic permeability. This requirement be addressed in the CSPEC and is currently approved to 1.03 µ in RFD-14-011. In addition, drawings revised to show the bearing plate details for the Type C4 through C6 castings (ECN-5059R3 change). SE141-139 thru -142 created to show the bearing plate details for the Type B and A castings, respectively.

ENGINEERING CHANGE PROPOSAL: NA DATE: 4/20/2006 (Rev 3)

COGNIZANT INDIVIDUAL MAKING THE CHANGE:

RESONSIBLE LINE MANAGER:

RLM Comments: This Rev 3 ECN will NOT be immediately incorporated. Rather a stamp will be placed on this drawing as Rev 2-a to drawings SE141-137 and SE141-138, to indicate that this ECN is outstanding.