PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 5023

COGNIZANT INDIVIDUAL:	D. Williamson

ECN TITLE:  Cable Connector Revision

ASSOCIATED ECP:  None

CC/WP/Job:	1403		     	AREA OR PROJECT:    NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __________________________________

(Signature indicates that no Work Planning form is required.)

If non-concurrence or associated with a work planning form, enter the WP Number:

| DRAWING(S) AFFECTED NUMBER: | NEW Revision | TITLE |
| --- | --- | --- |
| SE142C-059 | 1 | TYPE-C CABLE CONNECTOR DETAIL |
| Continued on Back |

DESCRIPTION OF CHANGE: (State Drawing No., Zone/Group, or List Attachments) QUAD C7 – Changed bore diameter from .41 to .44-in QUAD E7 – Added .03 x 30° chamfer QUAD C6 – Added machine finish symbol QUAD G3 – Added note re silver plating

PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN #5023

REASON FOR CHANGE: Modifications based on twisted racetrack (TRC) experience.

ENGINEERING CHANGE PROPOSAL: DATE: 9/8/05 N/A

COGNIZANT INDIVIDUAL MAKING THE CHANGE: D. Williamson

RESONSIBLE LINE MANAGER: B. Nelson