PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN # 5064R1

COGNIZANT INDIVIDUAL:	D. Williamson

ECN TITLE:  Revisions to Improve MCWF Machining/Inspection

ASSOCIATED ECP:  None

CC/WP/Job:	1403		     	AREA OR PROJECT:    NCSX

LIMITATION OF SCOPE - NOTE: A Work Planning Form is NOT required if the total change to be accomplished (ENG-032):

- Is not large or complex or does not represent a new installation into a usable space

- Does not have a significant ES&H impact

- Does not involve tritium or other radioactive contaminated or activated equipment

- Does not impact multiple projects, systems, or groups

OR does not change the scope or intent of the original design.

Responsible Line Manager CONCURRENCE: __________________________________

(Signature indicates that no Work Planning form is required.)

If non-concurrence or associated with a work planning form, enter the WP Number:

| DRAWING(S) AFFECTED NUMBER: | NEW Revision | TITLE |
| --- | --- | --- |
| SE141-114 | 6 | PRODUCTION WINDING FORM TYPE-A |
| SE141-115 | 6 | PRODUCTION WINDING FORM TYPE-B |
| SE141-116 | 8 | PRODUCTION WINDING FORM TYPE-C |
| Continued on Back |

DESCRIPTION OF CHANGE: (State Drawing No., Zone/Group, or List Attachments) Drawing changes reflect discussions held at Major Tool, Jan 4-6, 2006. See attachment for meeting summary and action items. Some changes were implemented through RFD-14-012 and -013. This ECN incorporates those changes also. Item #2b, Wing Surfaces Machining - References dwg SE141-114, -115, -116, SHT-1, G-2 References SE141-114/SHT-10/D5, SE141-115/SHT-11/C3, SE141-116/SHT-10/C4 Action is to change wing surface tolerance from +/-.125 to -.12/-.25-in. Item #3b, Flange Holes – References SE141-114/SHT4-5, SE141-115/SHT4-5, SE141-116/SHT4-5 Action is to change cylindrical zone tolerance from .01 to .06 and diam from 1.88+/-.01 to 1.885+/-.003-in. Item #4b, Tee Holes – References SE141-114/SHT2, SE141-115/SHT2, SE141-116/SHT2, DETAIL-C Action is to change cylindrical zone tolerance from .01 to .06-in. Item #5, Tee Profile- References SE141-114/SHT2, SE141-115/SHT2, SE141-116/SHT2, DETAIL-A Action is to change profile tolerance on top of tee web to .100-in total, change profile tolerance below VPI groove from .100 to .200-in. Leave “L” surface profile tolerance as is. Item #6, Tee Base Grinding- References SE141-114/SHT2, SE141-115/SHT2, SE141-116/SHT2, DETAIL-A Add note, “GRIND BASE OF TEE TO GIVE ACCESS FOR STUD WELDING. CLEARENCE DEFINED BY TEMPLATE, SE141-130, OVER ENTIRE LENGTH OF COIL.” Item #12, Port Openings References SE141-114/SHT7-8, SE141-115/SHT7-8, SE141-116/SHT7-8 Revise geometry to match hole cuts made using a single setup, change dimensions to reference or increase tolerance to be greater than drawing sheet tolerance. Item #13, Spherical Seats References SE141-114/SHT4-5, SE141-115/SHT4-5, SE141-116/SHT4-5 Change feature to conical seat, 1.38 diam x 1.25 dp, chamfer 1.88 diam x 90-deg. Change position tolerance from .01 to .06-in. Item #1, RFD-14-012, Flange Profile Tolerance References SE141-114/SHT10, SE141-115/SHT11, SE141-116/SHT10 Eliminate profile tolerance note for flanges, or change to .030-in total. T. Brown, PPT Slide, “added_chamfer_to_type-c_wing.ppt”, 12/16/05 References SE141-116/SHT1/C3 Add chamfer, 1. x .38 x ~9 LG to improve mod coil clearance at assembly.

PPPL ENGINEERING CHANGE NOTICE (ECN)   ECN #5064

REASON FOR CHANGE: Improve machining operations and overall schedule.

ENGINEERING CHANGE PROPOSAL: N/A DATE: 2/7/06

COGNIZANT INDIVIDUAL MAKING THE CHANGE: D. Williamson

RESONSIBLE LINE MANAGER: B. Nelson