| NATIONAL COMPACT STELLARATOR PROJECT Engineering Change Proposal (ECP) |
| --- |
| COVER PAGE (TO BE COMPLETED BY SYSTEMS ENGINEERING SUPPORT MANAGER) |
| Originator: David Williamson | Date: June 28, 2004 |
| ECP No: ECP-04-010 Revision 1 | ECP Title: Prototype Winding Form Poloidal Break Geometry |
| Required Reviewers |
| Required Reviewers for this ECP: P. Heitzenroeder |
| ECP Approval Level Expedited ECP? Yes No Change Level: Approving Official: |
| Actions Update CSPEC NCSX-CSPEC-141-01-04 Update drawing SE141-116P to reflect approved changes |
| APPROVALS (TO BE COMPLETED BY APPROVING OFFICIALS) |
| Change Level | Approving Official | Approval? | Signature |
| 3 | NCSX Project Manager | Yes No |  |
| 3a (Expedited ECP) | NCSX Engineering Manager | Yes No |  |
| 2 | NCSX Federal Project Director | Yes No |  |
| 1 | Associate Director OFES | Yes No |  |
| 0 | Under Secretary of Energy | Yes No |  |

| NATIONAL COMPACT STELLARATOR PROJECT Engineering Change Proposal (ECP) |
| --- |
| PART I (TO BE COMPLETED BY ORIGINATOR) |
| Originator: David Williamson | Date: |
| Overview of Change Type of ECP: EXPEDITED STANDARD Type of Change: TECHNICAL COST SCHEDULE EDITORIAL (Check all that Apply) Reason for Change: Vendor recommends 2.25-in cut through entire winding form section as a means of simplifying the shim geometry and improving fit-up of the shim, insulators, and bolts. Impacted WBS Elements: WBS 141 Modular Coil Winding Form Impacts of Change (Briefly Describe): This change will: Improve the shim and installation fit-up Remove the jog in the insulation path Will result in an increased width of the cut at the tee web (plasma side) Will not have a cost or schedule impact. Assessment of Other Options: None Detailed Description of the Change: (Use Continuation Sheets and/or Attach Information/Sketches, As Needed) List Attachments, Impacted Documents, etc. Drawing SE141-116P, Rev-1 incorporates these changes. Description of Change: SE141-116P, Sheet 1, Quad B2 – changed weight from 5575-lbs to 5104-lbs SE141-116P, Sheet 1, Quad A2 – Added typed name/date to drawing approval column SE141-116P, Sheet 7, Quad C5 – changed 0.75-in cut to 2.25-in cut thru SE141-116P, Sheet 7, Quad D2 – added Section C-C SE141-116P, Sheet 7, Quad C7– changed 90-deg to basic dimension SE141-116P, Sheet 7, Quad C3– changed 15-deg to basic dimension SE141-116P, Sheet 7, Quad H3 – changed hole position dimension from 1.50-in to 1.65-in – (added by Rev 1) SE141-116P, Sheet 7, Quad H5 – changed hole size from 1.50-in to 1.625-in diameter thru (added by Rev 1) |